## Slide 1: Packet Scheduling in Linux

## Slide 2: Traffic Control in Linux
The Linux operating system provides a series of traffic control algorithms for
  Scheduling
  Shaping
  Policing
  Dropping
Configuration utility is tc (traffic control), which is part of the iproute2
This presentation is focusing on scheduling

## Slide 3: Linux Scheduling Architecture
Non-default scheduling algorithms are provided as part of the iproute2 package

## Slide 4: Scheduling Algorithms
Default scheduling algorithm is FIFO
Others that are available:
  TBF – Token Bucket Filter
  PRIO – Static priorities
  SFQ – Stochastic Fair Queueing
Hierarchical scheduling algorithms
  HTB – Hierarchical Token Bucket
  CBQ – Class-based queueing
  HFSC – Hierarchical Fair Service Curves
Also:
  Netem – Add delay to a packet, limit throughput

## Slide 5: Linux Scheduling
A packet scheduler is referred to as a qdisc
Qdisc can be attached to a network device to schedule outgoing traffic
We consider the loopback device
  It is a virtual device with IP address 127.0.0.1.
  Packets sent to loopback are bounced back to the sending host

## Slide 6: Linux Scheduling
For configuration purposes, each device has a root
A qdisc is attached to the root
Each qdisk is assigned a handle, e.g., 2:0 or 2:
If a qdisc has traffic classes, each class also gets a handle, e.g., 2:1

## Slide 7: Token Bucket Filter (TBF)
Token bucket specification has three parameters:
  Rate (rate)
  Size of token bucket (burst)
  Buffer size (limit)
$ sudo tc qdisc add dev ifb0 root handle 1: \ tbf rate 10Mbit burst 10k limit 1M

## Slide 8: Traffic classes
Some qdiscs, e.g., FIFO are classless, others have traffic classes
For some qdiscs, e.g., PRIO, classes are implicitly defined
For other classful qdiscs, classes must be specified
There are different types of classes, and a class object must match the qdisc object for which it is defined
Some qdiscs, e.g., HTB, have a hierarchy of classes

## Slide 9: Handles
Handles are unique identifiers for Qdiscs and traffic classes
A handle consists of two numbers major and minor separated by “:” major:minor
A Qdisc has minor number set to 0, written as major:0 or major:
Traffic classes have the major number of the qdisc and a minor number, e.g., 2:1, 2:2, 2:3
This is a useful convention. The strict rule is that classes from the same Qdisc must have the same major number.

## Slide 10: Linux Scheduling: Example
$ sudo tc qdisc add dev lo root handle 2: prio
Adds a static priority scheduler to the loopback device
By default, there are three priority classes

## Slide 11: A qdisc can be attached to (other) qdisc’s
$ sudo tc qdisc add dev lo root handle 1: \ tbf rate 10Mbit burst 10k limit 1M
$ sudo tc qdisc add dev lo parent 1: handle 2: prio
Token bucket (TBF) is set to a rate limit of 10 Mbps.
Scheduling is static priority (with 3 priority levels)
Prio is attached to TBF
  any packet transmitted out of prio will go through TBF

## Slide 12: Token Bucket Filter (tbf)
$ sudo tc qdisc add dev lo root handle 2: tbf limit 50000 burst 1000 rate 2mbit
Token Bucket Filter with
  50KB max. backlog size (in buffer),
  bucket of size 1000 bytes,
  rate is 2Mbps

## Slide 13: Network emulator (netem)
Not a scheduler or shaper
It is a component that emulates what happens in a real network:
  adds delay,
  Imposes rate limit,
  simulates random packet drops,
  etc.
$ sudo tc qdisc add dev lo root handle 2: netem rate 50Mbit
Limits the transmission to a rate of 50 Mbps

## Slide 14: Deficit Round Robin (DRR)
A Round Robin scheduler which keeps tracks of transmitted bytes
  One FIFO queue for each flow
  Operates in “rounds”, where each queue with a backlog is visited once in a round
  Qi : Quantum of flow Maximum number of bytes from flow i that are sent in one round
  (Quantum is greater than max. size of flow i packets (Qi > Limax))
  DCi : Deficit counter of flow i Credit of flows (in bytes) saved for the next round
50
50
50
50
50
50
150
75
50
100
75
75
75
Credits
50
50
50
50
50
50
150
75
50
100
25
25
75
Credits
50
50
50
50
150
150
50
100
100
100
150
Credits
Time
Drawing from:https://web.stanford.edu/class/ee384y/projects/download03/francois_muralee.ppt

## Slide 15: Deficit Round Robin (DRR)
If queue is empty: Qi=0
Otherwise,
  Add quantum Qi to flow i in each round:
  DCi = DCi + Qi
  Transmit packet with size L from head of queue i and set
  DCi = DCi - L
  Continue transmitting (and subtracting DCi) until packet size at head of queue i is larger than DCi
15
50
50
50
50
50
50
150
75
50
100
75
75
75
Credits
50
50
50
50
50
50
150
75
50
100
25
25
75
Credits
50
50
50
50
150
150
50
100
100
100
150
Credits
Time
Drawing from:https://web.stanford.edu/class/ee384y/projects/download03/francois_muralee.ppt

## Slide 16: Deficit Round Robin (DRR)
$ sudo tc qdisc add dev lo root handle 1: drr
$ sudo tc class add dev lo parent 1: classid 1:1 drr
$ sudo tc class add dev lo parent 1: classid 1:2 drr
DRR is a classful scheduler
By default, the quantum is set to MTU
We need to explicitly define the classes

## Slide 17: Hierarchical Token Bucket (htb)
Traffic classes fall into multi-level hierarchy
Output of htb passes through a token bucket (which controls e maximum transmission rate)
Commands are given in lab/assignment handout

## Slide 18: Filters
Filters associate packets with a class
For scheduling, when a packet is added to a qdisc and the qdisc has classes, filters are applied to identify the class
Example:
Suppose we have three classes 2:1, 2:2, 2:3
$ sudo tc filter add dev lo parent 2: protocol ip u32 match ip dport 10000 0xffff classid 2:1
$ sudo tc filter add dev $INT parent 2: protocol ip u32 match ip dport 10001 0xffff classid 2:2
$ sudo tc filter add dev $INT parent 2: protocol ip u32 match ip dport 10002 0xffff classid 2:3
These filters map packets based on destination ports: 10000  2:1, 10001  2:2, 10002 2:3

## Slide 19: Filters (2)
Multiple matches:
  Filters are checked in order, until the first filter matches a packet. If there are multiple filters that match the packet, only the first one is applied
  Default may be overridden by a `prio` option.
No match
  Each qdisc has its own, default filter. If no user-provided filter matches, the filter of the qdisc is used
  (Some schedulers, e.g., DRR, drop packets that do not math any filter)

## Slide 20: Gotcha: Units
Be careful with declaring units in tc.
Rate:
  “kbit”  kilobit/sec
  “kbps”  kilobyte/sec
Size:
  “kbit”  kilobits
  “kb”, “k”  kilobytes
The same with M (mega), and G (giga).

## Slide 21: Gotcha
Delete an old qdisc before inserting new ones
  Sometimes you’ll stumble upon “RTNETLINK answers: File exists”. This means you’re trying to add qdisc to an occupied spot
  Fixes
    Remove the old qdisc first, using “tc qdisc del”
    Use “tc qdisc replace” instead of “tc qdisc add”
$ sudo tc qdisc del dev lo root
Deletes all qdiscs and classes on the loopback interface