## Slide 1
Elements of Application-layer Internetworking
Jorg Liebeherr University of Toronto
"Elements of Application-layer Internetworking for Adaptive Self-organizing Networks,” J. Liebeherr, M. Valipour, T. Y. Zhao, Proceedings of the IEEE, April 2019.

## Slide 2: The Internet began small …

## Slide 3: … to become one of the largest engineering artifacts in history
You are here

## Slide 4: In the Beginning...
There were many competing networks & architectures.
DataPAC
TransPAC
ARPANet
DECNet

## Slide 5: "Internetwork Layer"
IP started out as an overlay, designed to interconnect all kinds of other networks – both LANs and WANs.
DataPAC
IP Gateway
IP Gateway
TransPAC
ARPANet
DECNet
K. Calvert, ICNP 2017 Panel (used with permission from author)

## Slide 6: "Internetwork Layer"
...most of those underlying technologies faded away.
DataPAC
TransPAC
ARPANet
As router technology matured...
DECNet
"Network Layer"
K. Calvert, ICNP 2017 Panel (used with permission from author)

## Slide 7: "Hollowing Out"
Software-Defined Networking replaces routers with switches that are [semi]-oblivious to protocol standards.
K. Calvert, ICNP 2017 Panel (used with permission from author)

## Slide 8
This allows the domain owner to define the semantics of header bits – inside the domain...
... and leaves the inter-domain interface to ossify.
"Network Layer"
"Internetwork Layer"
K. Calvert, ICNP 2017 Panel (used with permission from author)

## Slide 9: Internet Infrastructure (the way I teach it)

## Slide 10: Internet Infrastructure (after a reality check)
Special purpose infrastructure 1
Special purpose infrastructure 2
Vehicular Net
5G Net
MANET
Private IP Net
IoT Net

## Slide 11: The Times They Are A-Changin'
Internet-centric: All infrastructures connect to the Internet, but not to each other
No central network:

## Slide 12: Internetworking today
Internet ossification since early 2000s
  global upgrades fail or proceed at glacial speed
Proliferation of proprietary infrastructures
Networks may not need access to Internet
Global addresses not always essential
No internetworking solutions for IoT devices
Lack of internetworking for mobile networks
 A good time to think about new approaches to Internetworking

## Slide 13: Application-layer Internetworking
Devices use available infrastructures to form a network
Separate network for each networked application
Each device can participate in arbitrarily many networks
Self-organizing:
  Devices detect and establish connectivity with other devices
  No central control
Networks may exist only for a limited time
Topology can be highly dynamic
All network nodes participate in relaying data (peer-to-peer)
No need for global deployment

## Slide 14: Multi-substrate application network
Collection of substrate networks
Application network

## Slide 15: Platform: HyperCast
HyperCast is a set of protocols for large-scale self-organizing application networks
Designed in my research group at Univ. of Virginia and Univ. of Toronto
~100,000 lines of Java
Socket inspired API

## Slide 16: HyperCast Application Networks
Applications self-organize to form a network graph
Data is forwarded along the edges of the graph

## Slide 17: Scalability Experiment
Experimental Platform: Linux PC Cluster
  up to 100 PCs
  Up to 100 nodes per PC
     up to 10,000 network nodes

## Slide 18
Experiment: Scalability
Measurement: Starting with N members, how long does it take to add M new members? Topology: Delaunay Triangulation
Time to Stabilize (sec)
Final number of nodes (N+M)

## Slide 19: Overlay Sockets

## Slide 20: Overlay Sockets
Substrate 1
Substrate 2
Substrate 3

## Slide 21: Writing Programs with Overlay Sockets
//Generate the configuration object OverlaySocketConfig ConfObj = OverlaySocketConfig.createOLConfig("hypercast.xml");
//Create an overlay socket I_OverlaySocket socket=ConfObj.createOverlaySocket(null);
//Join an overlay socket.joinOverlay();
//Create a message OL_Message msg = socket.createMessage(byte[] data);
//Send the message to all members in overlay network socket.sendToAll(msg);
//Receive a message from the socket OL_Message msg = socket.receive();
//Extract the payload byte[] data = msg.getPayload();
Similarities to Berkeley Socket API
Programs are independent of overlay topology and substrate network
Arbitrary number of overlay sockets per applicaiton

## Slide 22: Cross-Substrate Advertising
Notes: Internet Protocol Television

## Slide 23: Cross-substrate advertising
Example 1:
A and B prefer Substrate 1, but does not have address of A
Use Substrate 2 for rendezvous, and exchange address information about Substrate 1
B
Substrate 1 (Internet)
A
Substrate 2
Addr_A
Hello
Hello (+ Addr_A)
Hello
Notes: Hello

## Slide 24: Cross-substrate advertising
Example 2:
C joins network via Substrate 3 with B as neighbor
C prefers A as neighbor in the application network
C detects that it can talk to A via Substrate 2
B
C
Substrate 3
Substrate 1
A
Substrate 2 (no broadcast)
Addr_A

## Slide 25: Cross-substrate advertising - Outgoing -
myLA = 50,102
Source: 50,102
Adr_1
Adr_2
Adr_3
Adr_1
Adr_2
Adr_3
List of substrate addresses
Source: 50,102
Adr_1
Adr_2
Adr_3

## Slide 26: Cross-substrate advertising - Incoming -
LA | Substrate addresses
50,102 | Adr_1, Adr_2, Adr_3
Source: 50,102
Source: 50,102
Adr_1
Adr_2
Adr_3

## Slide 27: Different Methods for Cross-substrate Advertisement
Exchange address lists periodically
Attach address lists to protocol messages
Add address list to each message with info on node
Request address list when info is needed
Add preferred address to each message with info on node
“Push”
“Pull”
“Push Single”
Gossip
Protocol-driven dissemination

## Slide 28: Experimental Evaluation
Local Emulab Testbed
20 Linux nodes
Software:
  Hypercast with CSA
  Delaunay Triangulation protocol
  Multiple UDP/IP substrates
CPU | 2xQuad-Core Xeon 5400 (2 Ghz)
RAM | 4G DDR2
Interface | 8x1Gbps (4 Intel card, 4 NetFPGA)

## Slide 29: Experimental Evaluation
N x N substrates  (N+1) x (N+1) regions
Nodes equally distributed across regions
N=2
S1
S2
S4
S3
R11
R22
R12
R13
R23
R31
R21
R33
R23

## Slide 30: Mapping of Nodes to Substrates
K x K substrates  (K+1) x (K+1) regions
Nodes distributed uniformly across regions
K=2
S1
S2
S4
S3
R11
R22
R12
R13
R23
R31
R21
R33
R23

## Slide 31: Convergence
Percentage of stable nodes: K=17(289 substrates), 2592 nodes
Push/Pull
None
Push-single
Gossip
Push-single and gossip
250 ms
500 ms
1000 ms

## Slide 32: CSA Overhead
Received Traffic (average per node): K=17(289 substrates), 2592 nodes

## Slide 33: Internetworking with IoT devices
Notes: Internet Protocol Television

## Slide 34: Putting Internetworking in the Internet-of-Things
Today:
  IoT networks are “shrinkwrapped” products
  Consideration of networking only between IoT device and gateway
  Wide-area solutions are proprietary
Question:
  Is it feasible to build application-layer internetworks involving low-power IoT devices?
Challenge:
  Limited capabilities of IoT devices

## Slide 35: Internetworking with IoT devices
LoRa Feather board:
Microcontroller (no OS!)
<10 kbps
up to 500m with basic antenna
2K RAM
32K flash
Raspberry Pi with Lora shield:
Linux
1.2 GHz processor
1GB RAM
Modalities:
  Wifi
  Bluetooth
  LoRa

## Slide 36
Ongoing: Self-organizing multihop networking with LoRa
Date: July 17, 2019

## Slide 37: Conclusions
Application networks provide internetworking at upper layers
  easy to deploy
  self-organizing
Borrows heavily from self-organizing peer networks
Many interesting issues:
  Support in lower layers
  Adaptive services
  Limitations of IoT devices
  Security