## Slide 1: IoT and IP protocols
Professor Jorg Liebeherr

## Slide 2: IoT protocol stack
IPv4
IPv6
TCP
UDP
Application
6LoWPAN
Bluetooth / BLE
WiFi
COAP
MQTT
AMQP
HTTP
LoRa
LoRaWAN
Messaging Protocols
Transport Layer
Network Layer
MAC and PHY Layer
TCP/IP protocol stack
Zigbee
IEEE 802.15.4

## Slide 3: Background on IP networking
There are two versions of IP: IPv4 and IPv6
An IP address …
  … identifies a network interface
  … contains information to locate the interface
  … has 2 parts: network prefix and interface identifier
Dotted decimal notation of IPv4 addresses
CIDR notation of IP addresses

## Slide 4: Internet Protocol: Which version?
There are currently two versions of the Internet Protocol in use today:
IPv4 (IP Version 4)
    Specified in 1980/81
    Four byte addresses
    Universally deployed
    Problem: Address space almost exhausted
IPv6 (IP Version 6)
    Specification from 1998 (RFC 2460)
    16-byte addresses
    Several differences to IPv4, but no fundamental changes

## Slide 5: Dotted decimal notation
IPv4 addresses are written using dotted decimal notation:
      Each byte is written as a decimal number in the range [0..255], separated by periods (`dots’).
Example:
01100100
10000000
00001011
00111100
1st Byte
2nd Byte
3rd Byte
4th Byte
128.100.11.60
= 128
= 100
= 11
= 60

## Slide 6: Length of network prefix
IP address consists of a network prefix and an interface identifier:
      Network prefix determines an IP network (subnet)
      Interface identifier determines a network interface on the subnet
The prefix length must be provided with an IP address
Two conventions for indicating the prefix length:
    Add the prefix length measured in bits (CIDR notation, prefix notation, slash notation)
    Provide a bitmask of the prefix length in dotted decimal notation (netmask, subnetmask)
network prefix
interface identifier
32 bits
Prefix length

## Slide 7: Notation of IPv4 addresses
Example: Suppose the prefix length is 16 bits
CIDR notation: 128.100.11.60/16
Netmask notation: 128.100.11.60, 255.255.0.0

## Slide 8: IPv6 addresses
IPv6 addresses are 16 bytes (128 bits) long
IPv6 addresses are written as hexadecimals
“Blocks” of 16 bits are separated by colons
Abbreviations:
  Leading zeros in a block can be omitted
  One group of contiguous blocks with all zeros can be replaced by a double colon
FE80::2A:0:0:A81

## Slide 9: CIDR notation for IPv6 addresses
IPv6 addresses are written in CIDR notation
2607:F2C0:92C7:4A00:1053:D1D:66E9:41EA/64
The number after the slash (/) is the prefix length, which identifies the network part (network prefix)
All interfaces on the same subnet have the same network prefix
1053:D1D:66E9:41EA
2607:F2C0:92C7:4A00
prefix length
128 bits
64 bits
64 bits
Notes: RFC 3587 (earlier allocation was defined in RFC 2374)

## Slide 10: Types of IPv6 addresses
 | IPv6 Prefix
Global unicast | 2000::/3
Link-local unicast address | FE80::/10
Unique local unicast address (ULA) | FC00::/7
Multicast | FF00::/8
Broadcast: No broadcast address in IPv6
Anycast: Any unicast address can be designated as an anycast address

## Slide 11: Global unicast address (2000::/3)
Global routing prefix
   is allocated from an internet service provider (ISP) or registry (RIR)
  Typically, 32 ≤ N ≤ 64
Subnet ID is determined locally
Interface ID
   has length 64 bits
   is built using EUI-64 format (or alternative method)
Notes: RFC 3587 (earlier allocation was defined in RFC 2374)

## Slide 12: Link-local unicast address (FE80::/10)
IPv6 requires that each interface has a link-local address, even it has a global unicast address
Link -local address is used whenever communicating with nodes on same subnet
Packets with this address are local to a subnet (not forwarded by routers)
Interface ID is generated automatically, e.g., with EUI-64

## Slide 13: Unique Local Unicast Address (ULA) (FC00::/7)
ULA addresses play the same role as private addresses in IPv4
ULA addresses are intended for communication within an organization
Packets with this address may be routed within an administrative domain, but are not globally routable
Global ID is randomly selected

## Slide 14: MAC addresses
A MAC address is data link layer address of a NIC
  Also called “hardware address” or “physical address”
  Length of a MAC address is typically 6 bytes
MAC addresses are in hexadecimal notation, using “:” or “-” for byte separation: c8:2a:14:04:0a:81
    Set by manufacturer of NIC
    Intended to be permanent and globally unique
    Today, most hardware allows to change MAC addresses
Broadcast MAC address: ff:ff:ff:ff:ff:ff

## Slide 15: EUI-64 address
In IPv6, the interface ID is often an EUI-64 address
IEEE EUI-64 is essentially a 8-byte MAC address
EUI-64 address is created from a 48-bit MAC address
Notes: Why the ”flipped bit”?
The 7th bit of the 1st byte is designated as the U/L (Universal/Local) bit. If U/L=0, the address is globally unique. if U/L=1, the address is locally administered (possibly not globally unique).
MAC addresses of interface cards have U/L=0. So, when (locally) creating a EUI-64 for an IPv6 address, it makes sense to setting U/L=1. However, on a virtual machine the MAC addresses of the virtual interfaces are locally created, and, consequently, the MAC address has U/L=1. When creating an EUI-64 address, it would make sense to leave the value U/L=1. However, this is not what is happening. When creating an IPv6interface identifier, the EUI-64 address is set to U/L=0. This obviously does not make sense (since it declares a non-unique address to be globally unique).
It appears that no protocol ever makes a decision based on the U/L bit. So, this logical flaw has no impact.

## Slide 16: EUI-64 address
Rules:
Insert: FF:FE after 3rd byte
Invert 7th bit of 1st byte
In IPv6, the interface ID is often an EUI-64 address
IEEE EUI-64 is essentially a 8-byte MAC address
EUI-64 address is created from a 48-bit MAC address

## Slide 17: Assignment of addresses
MAC address is set by manufacturer of NIC
IPv4:
  Manual configuration
  DHCP (Dynamic Host Configuration Protocol)
   DHCP server assigns addresses
IPv6:
  Manual configuration
  DHCPv6  DHCP server assigns addresses
  Stateless autoconfiguration
    Router provides network prefix, host selects interface address
    No server is required

## Slide 18: IPv4 header format
20 bytes ≤ Header Size ≤ (24 -1) x 4 bytes = 60 bytes
20 bytes ≤ Total Length ≤ 216 -1 bytes = 65,535 bytes

## Slide 19: IPv6 header format
Note: There is no header size field. Headers (not including header extensions) are always 40 bytes

## Slide 20: IPv6 packet header
IPv6 has a simplified header structure:
  Headers have fixed size
  No fragmentation (available as option)
  No header checksum
Most fields play a similar role as in IPv4:
Flow label: Can be used by a source to label packets from the same flow
IPv6 | … similar to … | IPv4
Version |  | Version
Traffic class |  | DS
Payload length |  | Total length
Next Header |  | Protocol
Hop Limit |  | TTL

## Slide 21: Extension Headers
Instead of header options, IPv6 allows to concatenate optional headers to the main header
Extension Headers:
    Security: Authentication
    Fragmentation
    Routing
    Payload Header (TCP, UDP, …)

## Slide 22: Using IP protocols for IoT
Benefits
IoT devices can be accessed from global IP network (“Internet”)
Easy interconnection to other IP networks
Socket API for IP network programming is well understood
Challenges
Packet size
  MTU of IEEE 802.15.4: 127 bytes
  Min. MTU of IPv6: 1280 bytes
Address sizes
IP assumes that devices on a subnet can be reached with a link layer message
  Does not hold in multihop wireless networks

## Slide 23: Videos with additional information
IPv4 addresses
Subnetting
IPv6 addresses: Part 1, Part 2
IPv4 Protocol
IPv6 Protocol