## Slide 1: Web of Things
Professor Jorg Liebeherr

## Slide 2: IoT protocol stack
IPv4
IPv6
TCP
UDP
Application
6LoWPAN
Bluetooth / BLE
WiFi
CoAP
MQTT
AMQP
HTTP
LoRa
LoRaWAN
Messaging Protocols
Transport Layer
Network Layer
MAC and PHY Layer
TCP/IP protocol stack
Zigbee
IEEE 802.15.4

## Slide 3: Representational state transfer (REST)
REST is a software architecture for distributed systems designed to ensure interoperability
IoT messaging protocols are RESTful
REST design principles:
  Client/server architecture
  Statelessness
  Cacheable
  Layered system
  Uniform interface
Review: From earlier lecture …

## Slide 4: The Web of Things (WoT)
Concept: Use the Web to build applications for IoT
  Standardized by the W3C (World Wide Web Consortium)
Goal: The Web of Things (WoT) seeks to counter the fragmentation of the IoT by using and extending existing, standardized Web technologies
Examples: HTTP, JSON, RESTful APIs, and WebSockets
Original Approach: Each device is a web server  Access devices via web browsers
Today: Devices can be web servers, web clients, or both

## Slide 5: Web of Thing requirements (original approach)
Must be at least an HTTP/1.1 server
Must have a root resource accessible via an HTTP URL
Must support GET, POST, PUT, and Delete HTTP commands
Must implement certain HTTP status codes
Must support JSON as default representation
Must support GET on its root URL
Should support: support HTTPS, WebSocket, …
http://gateway.api.com/devices/TV
http://192.168.1.3:9002
https://kitchen:3000/fridge/root

## Slide 6: Key WoT Concepts
Standardized Communication Devices communicate using common web technologies
Thing Descriptions (TD) Standardized method to describe a device’s properties, actions, and events in JSON format
Interoperability WoT promotes compatibility across different platforms and devices
Decentralization Instead of a being cloud-based, WoT enables peer-to-peer interactions
Security & Privacy WoT integrates web security standards (OAuth, TLS)

## Slide 7: Thing Description
A Thing Description (TD) is a JSON representation describing capabilities of a Web Thing
View example at:
https://github.com/w3c/wot-thing-description/blob/main/proposals/simplified-td/example.json

## Slide 8: Direct connectivity between clients and Web Things
Source: http://model.webofthings.io/

## Slide 9: Cloud-based connectivity of Web Things
Source: http://model.webofthings.io/

## Slide 10: WoT Evolution
Pre-2010s: WoT uses an "every sensor as a server” model
  Limitations of this model:
    Resource constraints  sensors may not be able to run a web server
    Power constraints  sensors need to be powered on to allow access
    Network constraints  sensors may be behind a firewall or NAT
    Security constraints  sensors may not be able to run strong security protocols
2010s: Shift to gateway-based architectures ⟹ sensors are clients that send data to gateways or cloud service
Since 2015: Devices can be servers or clients → TD descriptions also for clients
2020: Latest W3C Web of Things (WoT) standard: TDs can include MQTT-based communications* *Interesting: MQTT is not a web protocol and does not follow a REST architecture

## Slide 11: Web of Things vs. Internet of Things
 | Internet of Things | Web of Things
Focus | Connecting devices to the internet | Using web technologies to improve accessibility
Protocols | Various (MQTT, CoAP, AMQP, …) | Web-based (HTTP, WebSockets, REST)
Interoperability | Limited (can be vendor-specific) | High (web standards)
Security | Custom security | Web security mechanisms