## Slide 1: Classful IPv4 Addresses
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Delivery modes: unicast, multicast, broadcast, anycast
IPv4 address classes (A, B, C, D, E)
With classful addressing, the prefix length is implied
Transition from classful addresses to CIDR

## Slide 3: Delivery methods
Unicast: one-to-one transmission
Broadcast: one-to-all transmission (with respect to a scope)
Multicast: one-to-many transmission
Anycast: one-to-any transmission
The Internet Protocols (IPv4 and IPv6) use different destination addresses for each delivery method
unicast
broadcast
multicast
anycast

## Slide 4: Classful addresses
When IPv4 was introduced (early 1980s), the Internet address space was divided up into 5 classes
The class is determined by the leading bits of an IPv4 address:
  Class A: The first bit of the IP address is “0”
  Class B: The first 2 bits of the IP address start with “10”
  Class C: The first 3 bits of the IP address start with “110”
  Class D: The first 4 bits of the IP address start with “1110”
  Class E: The first 4 bits of the IP address with “1111”

## Slide 5: Classful addresses
The prefix length of a (unicast) IPv4 address is implied by its class  No need to provide the prefix length with an IPv4 address
Three classes available for unicast:
  Class A: prefix length is 8 (/8 network)
  Class B: prefix length is 16 (/16 network)
  Class C: prefix length is 24 (/24 network)
Two additional classes:
  Class D: Multicast (group) addresses
  Class E: Reserved for future use

## Slide 6: Classful IPv4 addresses

## Slide 7: Classful IPv4 addresses
Class E addresses have never been released for use

## Slide 8: Division of the IPv4 address space
00000…00
Class A
(231 addresses)
10000…00
Class B
(230 addresses)
Class C (229 addresses)
11000…00
Class D (228 addresses)
11100…00
unused addresses
Class E (228 addresses)
11110…00

## Slide 9: Delivery methods and IPv4 address types
Unicast ✓
Broadcast ✓
Multicast ✓
Anycast ✕
unicast
broadcast
multicast
anycast
Class A, B, C addresses
Broadcast addresses (e.g.,255.255.255.255, 128.100.255.255)
Class D addresses
There are no anycast addresses in IPv4

## Slide 10: Limitations of classful IP addresses
Limited flexibility for obtaining a network address:
    Class C: 28 - 2 = 254 IP addresses are available
    Class B: 216 - 2 = 65,534 IP addresses are available
    Class A: 224 - 2 = 16,772,214 IP addresses are available
Too few network addresses for large networks
    27 = 128 Class A networks
    214 = 16,384 Class B networks
Flat address space. Routing tables in the backbone Internet need one entry for each network address.
  Class C networks: up to 221 = 2,097,152 entries

## Slide 11: Allocation of classful addresses

## Slide 12: From classful to classless addresses
  By the early 1990s, the lookup time of routing tables had become a bottleneck for Internet performance
  In 1993, there was a major shift for interpreting and allocating IP addresses:
until 1993:
Classful Addresses
after 1993:
Classless Interdomain Routing (CIDR)

## Slide 13: CIDR - Classless Interdomain Routing
CIDR abandons the fixed prefix lengths for classes A, B, and C
Key Concept: Prefix length can have any value
This is also called variable-length subnet masking (VLSM)
Consequences:
  Since the prefix length is no longer implied by the address, it must be provided with an IP address ( CIDR notation)
  Hierarchical routing aggregation introduces dependency of IP addresses to service provider
  Need for new lookup algorithms for routing tables