## Slide 1: Subnetting
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Subnetting = Dividing an IP network (subnet) into smaller networks
Subnetting is done by increasing the network prefix
An organization uses subnetting to create smaller networks for its organizational units
Subnetting is not visible outside the organization

## Slide 3: Network Prefix and Interface Identifier
IP address consists of a network prefix and an interface identifier:
CIDR notation: 128.100.11.60/16
Netmask notation: 128.100.11.60, 255.255.0.0

## Slide 4: Subnetting
UofT Network
128.100.0.0/16
Scenario: Organization has a large network prefix and wants to create smaller networks
  Subnetting: Use a portion of the interface identifier to identify a smaller network (“subnetwork”, “subnet”).
Each subnet becomes a separate network
Faculty of Engineering
128.100.11.0/24
Faculty of Arts and Science
128.100.58.0/24
Library
128.100.136.0/24
MIE
128.100.11.128/26
ECE
128.100.11.64/26

## Slide 5: Basic Idea of Subnetting
Split the interface identifier portion of an IP address into a subnet identifier and a (smaller) interface identifier.
Then:
    Subnets can be freely assigned within the organization
    Internally, subnets are treated as separate networks
    Subnet structure is not visible outside the organization
network prefix
interface identifier
subnet id
network prefix
interface id
extended network prefix

## Slide 6: Subnetmask
For the IP configuration, the subnet id becomes part of the network prefix
Device only knows about the extended network prefix
The netmask of the extended network prefix is called subnetmask
CIDR notation: 128.100.11.60/24
Netmask notation: 128.100.11.60, 255.255.255.0

## Slide 7: Example
IP address of host: 128.100.11.60
(original) network prefix: 128.100.0.0/16
Subnet number (with length 8 bit) : 11
CIDR notation of new network prefix: 128.100.11.0/24
    Address of host:
    CIDR notation: 128.100.11.60/24
    Netmask notation: 128.100.11.60, 255.255.255.0

## Slide 8: Advantages of Subnetting
With subnetting, IP addresses use a 3-layer hierarchy:
        Network prefix
        Subnet identifier
        Interface identifier
Subnetting reduces router complexity. Since router outside the organization do not need to know about subnetting, the complexity of routing tables at outside the organization is reduced.
Flexibility: Length of the subnet mask need not be identical on all subnetworks.

## Slide 9: Creating and Managing Subnets
Use of subnetting or length of the subnetmask is decided by the network administrator
Subnets are created by setting the subnetmask of an IP interface
Important: Subnetmasks must be set consistently

## Slide 10: No Subnetting
All hosts think that the other hosts are on the same network

## Slide 11: With Subnetting
Hosts with same prefix/subnetmask belong to the same network

## Slide 12: With Subnetting
Different subnetmasks lead to different views of the scope of the network

## Slide 13: Usage of “subnet” and “subnetmask”
Earlier, we used the term “subnet” even though there was no subnetting
This is a convention:
  The terms “subnet” or “IP subnet” are used to designate an IP network
  Also, “subnetmask” and “netmask” are often used interchangeably

## Slide 14: Every IP network is a subnet
The term “subnet” for an IP network is fitting since we can view every IP network as a subnet of a larger network
0.0.0.0/0
128.0.0.0/2 Class B
128.100.0.0/16 (UofT)
128.100.11.0/24