## Slide 1: Sep 16 Lecture
ECE 461 Fall 2020
Lecture starts 10 minutes after the hour
Tutorials also start 10 minutes after the hour

## Slide 2: Agenda
General questions
Finish discussion of labs (Lab information)
Slide sets “IPv4 Addresses,” “Classful Addresses,” “Subnetting”
  Walk through slides
  Take questions
  Checkpoint questions

## Slide 3: IP4v Addresses: Checkpoint 1
Write the IPv4 address, given in binary notation with indicated prefix length, in CIDR notation
110010110110010100 00101000001
Prefix length

## Slide 4: IPv4 Addresses: Checkpoint 2
Given the IPv4 address 10.2.254.72/22, write the network prefix and the interface identifier in binary
Notes: 10: 0000 1010
2: 0000 0010
254: 1111 1110
72: 0100 1000
Network prefix: 0000 1010 0000 0010 1111 11
Interface identifier: 10 0100 1000

## Slide 5: IP4v Addresses: Checkpoint 3
Given the IPv4 address block (a.k.a. network prefix, a.k.a. prefix) 10.2.128.0/22
  Provide the range of addresses in dotted-decimal notation?
  How many hosts (interfaces) can be added to this prefix?
Notes: a) Smallest: 10.2.128.0
Largest: all ones on interface identifer
Largest (3rd and 4th byte first written in binary): 10.2.1000 00 11.1111 1111  10.2.131.255
b) 10 bits available for interface identifier
Total addresses: 2^10 – broadcast – network address = 1024-2 = 1022

## Slide 6: IP4v Addresses: Checkpoint 4
Explain:
  loopback address
  link-local address

## Slide 7: Classful IPv4 Addresses: Checkpoint 1
Assume classful addresses. Write the following addresses in CIDR notation
  10.1.2.4
  151.101.1.67
  192.82.129.91
  239.3.2.1
Notes: Class A: 10.1.2.4/8
Class B: 151.101.67/16
Class C: 192.82.129.91/24
Class D: does not use CIDR notation

## Slide 8: Subnets: Checkpoint 1
Given the IPv4 prefix 10.2.128.0/22, create two subnets that can accommodate 500 and 200 hosts, respectively.
  Provide the network prefix for each subnet in CIDR notation
  Determine the maximum number of interfaces that can be placed on each subnet
  Provide the range of addresses for each subnet
  Provide the broadcast address for each subnet
Notes: a) There are multiple solutions.
500 hosts  next power of 2 is 512=2^9  needs /23
200 hosts -> next power of 2 is 256 = 2^8  needs /24
Subnet 1: 10.2.128.0/23
Subnet 2: 10.2.130.0/24
b) Subnet 1: /23 = 2^9 : subtract 2  510
Subnet 2: /24 =2^8: subtract 2  254
Subnet 1: 10.2.128.0 – 10.2.129.255 Subnet 2: 10.2.130.0 – 10.2.130.255