## Slide 1: TCP/IP Networking - An Example
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Multiple protocols are involved in delivering data

## Slide 3: A simple TCP/IP Example
A user on host argon.tcpiplab.edu (“Argon”) makes a web access to URL
http://neon.tcpip-lab.edu/index.html.
What actually happens in the network?

## Slide 4: HTTP Request and HTTP response
The web access is handled by the HTTP protocol:
GET /index.html HTTP/1.1
Accept: image/gif, */*
Accept-Language: en-us
Accept-Encoding: gzip, deflate
User-Agent: Mozilla/4.0
Host: neon.tcpip-lab.edu
Connection: Keep-Alive
HTTP request
HTTP/1.1 200 OK
Date: Sat, 25 May 2020 21:10:32 GMT
Server: Apache/1.3.19 (Unix)
Last-Modified: Sat, 25 May 2002 20:51:33 GMT
ETag: "56497-51-3ceff955"
Accept-Ranges: bytes
Content-Length: 81
Keep-Alive: timeout=15, max=100
Connection: Keep-Alive
Content-Type: text/html
<HTML>
<BODY>
<H1>Internet Lab</H1>
Click <a href="http://www.tcpip=lab.net/index.html">here</a> for the Internet Lab webpage.
</BODY>
</HTML>
HTTP response

## Slide 5: From HTTP to TCP
To send a request, the HTTP client program opens a TCP connection to the HTTP server at Neon
To create a TCP connection, a TCP client requires address information on the server, consisting of:
    a 32-bit IPv4 address
    a 16-bit port number

## Slide 6: Domain Name System (DNS)
Argon contacts a DNS server to translate the domain name neon.tcpip-lab.edu into an IP address
The Domain Name System (DNS) is a worldwide distributed system of DNS servers.
Each host that uses domain names must be configured with the IP address of a DNS server

## Slide 7: Port numbers
Port numbers are used to identify application programs on a client or server application
When a server application is started, it “binds” to a port number
For many services there are default port numbers (“well-known ports”):
  Hypertext transfer protocol http 80
  Hypertext transfer protocol secure https 443
  Telnet telnet 23
  Secure shell ssh 22
In the example, Argon uses the well-known port for http

## Slide 8: Opening a TCP Connection
  The HTTP client at Argon requests to open a TCP connection to port 80 at 128.143.71.21
  How is this done?
    The HTTP client requests its local TCP protocol to open a connection to port 80 at 128.143.71.21

## Slide 9: Opening a TCP Connection
  The TCP protocol at Argon wants to open a connection to port 80 at 128.143.71.21
  How is this done?
    The TCP protocol requests its IP protocol to send an IP datagram to 128.143.71.21
    The IP datagram contains the connection request.

## Slide 10: Sending the IP datagram to an IP router
Argon (128.143.137.144) can deliver the IP datagram directly to Neon (128.143.71.21), only if both are on the same subnet
  This is where the subnetmask comes in
  Argon has a /24 address
Here, Argon and Neon are not on the same subnet
  Since the IP address of Neon does not match Argon’s on the first 24 bits
Argon sends the IP datagram to its default gateway
    The default gateway is an IP router
    The IP address of the default gateway must be configured
    Argon’s default gateway has IP address 128.143.137.1

## Slide 11: The route from Argon to Neon
Note that the IP router has a different IP address for each of its interfaces

## Slide 12: Sending packet over an Ethernet network
Situation: Argon wants to send an IP datagram to its default gateway
Since Argon’s network interface is to an Ethernet network, Argon puts the IP datagram in an Ethernet frame
Ethernet uses MAC addresses  Argon must first translate the IP address 128.143.137.1 into a MAC address
    This is done with the Address Resolution Protocol (ARP)

## Slide 13: Address resolution with ARP

## Slide 14: Sending an Ethernet frame
Now the Ethernet frame can be sent

## Slide 15: Forwarding the IP datagram
When Router137 receives the Ethernet frame, it recovers the IP datagram and determines that the IP datagram should be forwarded to the interface with name 128.143.71.1
The IP router determines that it can deliver the IP datagram directly

## Slide 16: Another lookup of a MAC address
The router needs to find the MAC address of Neon
Again, ARP is invoked, to translate the IP address of Neon (128.143.71.21) into the MAC address of neon (00:20:af:03:98:28)

## Slide 17: Sending another Ethernet frame
Router71 sends the Ethernet frame to Neon

## Slide 18: Wrapping-up the example
So far, Neon has only obtained a single packet
Much more work is required to establish an actual TCP connection and the transfer of the HTTP Request
The example was simplified in several ways:
No transmission errors
The route between Argon and Neon is short (only one IP router)
Argon knew how to contact the DNS server (without routing or address resolution)
….