## Slide 1: Review of Networking Concepts
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Review:
  Layered protocol suite
  Interactions between layered protocols
  Encapsulation and decapsulation

## Slide 3: Sending a packet from Argon to Neon

## Slide 4: Sending a packet from Argon to Neon
DNS: The IP address of “neon.tcpip-lab.edu” is 128.143.71.21
ARP: What is the MAC address of 128.143.137.1?
DNS: What is the IP address of “neon.tcpip-lab.edu”?
ARP: The MAC address of 128.143.137.1 is 00:e0:f9:23:a8:20
128.143.71.21 is not on my subnet.
Therefore, I need to send the packet to my
default gateway with address 128.143.137.1
frame
128.143.71.21 is on one of my local subnets.
Therefore, I can send the packet directly.
ARP: The MAC address of 128.143.137.1 is 00:20:af:03:98:28
ARP: What is the MAC address of 128.143.71.21?
frame

## Slide 5: Internet protocol suite
The Internet protocol suite is the protocol architecture of the Internet
The Internet protocol suite has four layers: Application, Transport, Internet, and Link Layer
A host implements all layers. Routers only have link and Internet layers
Note:
  Internet protocols do not actually specify a link layer
  They specify how to interface with existing link layers

## Slide 6: Internet protocols and OSI reference model
The Internet protocols do not define the lower layers of a complete protocol stack
Layer 7
Layer 6
Layer 5
Layer 4
Layer 3
Layer 2
Layer 1

## Slide 7: Assignment of protocols to layers

## Slide 8: Layered communications
A module of a given layer communicates with:
  1. a remote module a the same layer using a common protocol
  2. adjacent module at the local system via a service interface
Node A
Node B

## Slide 9: Layers in the example

## Slide 10: Layers in the example
Send HTTP Request to neon
Establish a connection to 128.143.71.21 at port 80
Open TCP connection to 128.143.71.21 port 80
Send a datagram (which contains a connection request) to 128.143.71.21
Send IP datagram to 128.143.71.21
Send the datagram to 128.143.137.1
Send Ethernet frame to 00:e0:f9:23:a8:20
Send Ethernet frame to 00:20:af:03:98:28
Send IP data-gram to 128.143.71.21
Send the datagram to 128.143.7.21
Frame is an IP datagram
Frame is an IP datagram
IP datagram is a TCP segment for port 80

## Slide 11: Encapsulation and decapsulation
As data is moving down the protocol stack, each protocol adds layer-specific control information

## Slide 12: Encapsulation and decapsulation in the example
Let us look in detail at the Ethernet frame between Argon and the Router, which contains the TCP connection request to Neon.
This is the frame in hexadecimal notation.
00e0 f923 a820 00a0 2471 e444 0800 4500 002c 9d08 4000 8006 8bff 808f 8990 808f 4715 065b 0050 0009 465b 0000 0000 6002 2000 598e 0000 0204 05b4

## Slide 13: Parsing the information in the frame

## Slide 14: Encapsulation and decapsulation

## Slide 15: Encapsulation and decapsulation: Ethernet header

## Slide 16: Encapsulation and decapsulation: IP header

## Slide 17: Encapsulation and decapsulation: IP header

## Slide 18: Encapsulation and decapsulation: TCP header
Option: maximum segment size

## Slide 19: Encapsulation and decapsulation: TCP header

## Slide 20: Encapsulation and decapsulation: TCP header

## Slide 21: Encapsulation and decapsulation: Application data
No Application Data
in this frame

## Slide 22: Different views of networking
Different Layers of the protocol stack have a different view of the network. This is HTTP’s and TCP’s view of the network

## Slide 23: Network view of IP

## Slide 24: Network view of Ethernet