## Slide 1: Data Link Protocols
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Types of data link networks
Format of a MAC address
Difference between an Ethernet switch and Ethernet hub
Format of Ethernet frames
Types of point-to-point links

## Slide 3: Internet protocol suite
The Internet protocol suite does not define data link and physical layers
Instead it takes advantage of existing lower layers, and defines interfaces to access them
Data link layers are specified by other bodies (e.g., IEEE 802)
In Internet terminology, any data link network is referred to as a “link”

## Slide 4: Data link layer (Layer 2)
The main tasks of the data link layer are:
    Transfer data from the network layer of one node to the network layer of another node
    Convert the raw bit stream of the physical layer into groups of bits (frames)

## Slide 5: Types of networks at the data link layer
  Broadcast networks: All stations share a single communication channel
    Most local area networks (LANs), e.g., Ethernet and WiFi, are broadcast networks
    Needs addresses, e.g., MAC addresses
  Point-to-Point networks: Pairs of hosts (or routers) are directly connected
    Wide area networks (WANs) are mostly point-to-point
    Addresses are not needed

## Slide 6: Medium Access Control (MAC)
In a broadcast network, the stations must ensure that only one station transmits at a time on the shared communication channel
Protocols to determine who can transmit at any time are called Medium Access Control (MAC) protocols
  Ethernet: CSMA/CD
  WiFi: CSMA/CA
MAC protocol is running on a NIC (network interface controller):
  NIC has a MAC address
Ethernet NIC

## Slide 7: MAC Addresses
A MAC address is an address of a NIC
  Also called “hardware address” or “physical address”
  Length of a MAC address is typically 6 bytes
MAC addresses are in hexadecimal notation, using “:” or “-” for byte separation: c8:2a:14:04:0a:81
    Set by manufacturer of NIC
    Intended to be permanent and globally unique
    Today, most hardware allows to change MAC addresses
Broadcast MAC address: ff:ff:ff:ff:ff:ff
Multicast MAC address: Last bit of first byte is set to “1”

## Slide 8: Ethernet Topology
There are many (>50) Ethernet variants
  Speed: 2 Mbps - 400 Gbps
  Frame formats: 802.3, Ethernet II (DIX)
Ethernet was originally designed as a bus topology
Since mid-1990s, nodes are connected to a hub or switch in a star configuration

## Slide 9: Ethernet Hubs vs. Ethernet Switches
Ethernet switch
Packet switch for Ethernet frames
Has routing table based on MAC addresses
Buffering of frames prevents collisions
Ethernet hub
Does not perform buffering
Collisions occur if two frames arrive at the same time
Frame that arrives on one port is sent out on all ports
Hub
Switch

## Slide 10: Two Ethernet frame formats
Two Ethernet frame formats are in use, with subtle differences:
  Ethernet II (DIX)
    An industry standard from 1982 that is based on the first implementation of CSMA/CD by Xerox.
    Most commonly used format
  802.3:
    IEEE’s version of CSMA/CD from 1985.
Difference for our purposes: Ethernet II and 802.3 use different methods to encapsulate IP datagrams

## Slide 11: Ethernet II encapsulation (RFC 894)

## Slide 12: IEEE 802.2/802.3 encapsulation (RFC 1042)
destination address, source address: 48-bit MAC address
length: frame length in bytes
DSAP, SSAP: set to 0xAA
control: set to 3
OUI: set to 0 Ethertype: same as in Ethernet II
CRC: cyclic redundancy check
38-1492

## Slide 13: Point-to-point links
Many data link connections are point-to-point serial links:
  Dial-in or DSL access connects hosts to access routers
  Long-distance links
Data link layer protocols for point-to-point links are simple:
  Main role is encapsulation of IP datagrams
  No media access control needed
  No address needed

## Slide 14: Data link protocols for point-to-point links
HDLC (High-Level Data Link)
  Widely used and influential standard (1979)
  Default protocol for serial links on Cisco routers
PPP (Point-to-Point Protocol)
  Based on a variant of HDLC
  Used for dial-in and for high-speed routers
Ethernet point-to-point
  Used for long-distance point-to-point links (up to 100 Gbps)

## Slide 15: PPP - IP encapsulation
The frame format of PPP is similar to HDLC and the 802.2 LLC frame format:
PPP assumes a duplex circuit
Note: PPP does not use addresses
Usual maximum frame size is 1500
Notes: PPP suports an asynchronous link (8 data bits/no parity) or a bit-oriented synchronous link

## Slide 16: Additional PPP functionality
In addition to encapsulation, PPP supports:
  Link configuration
  Link quality testing
  Error detection
  Option negotiation
  Address notification
  Authentication
The above functions are supported by helper protocols:
  LCP
  PAP, CHAP
  NCP

## Slide 17: Tunneling protocols
Tunnels are logical point-to-point links
  They appear to the endpoints as a point-to-point links
  The link is realized as a sequence of subnets

## Slide 18: Switched networks
Some data link technologies can be used to build complete networks, with their own addressing, routing, and forwarding mechanisms.
These networks are often called switched networks
At the IP layer, a switched network may appear as a point-to-point link or a broadcast link

## Slide 19: Switched networks
Data link layer technologies:
  Switched Ethernet
  Multiprotocol Label Switching (MPLS)
  ATM (Asynchronous Transfer Mode)
  Frame Relay
Some switched networks are intended for enterprise networks (Switched Ethernet), wide area networks (MPLS, Frame Relay), or both (ATM)