## Slide 1: Neighbor Discovery Part 1
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Roles of neighbor discovery (ND) and address resolution
Address resolution in IPv4 (ARP)
Address resolution in IPv6 (NDP)
Address resolution for multicast

## Slide 3: Neighbor discovery
Neighbor discovery refers protocol functions that determine link-layer addresses of nodes that are attached to the same link
In IP terminology, “link” refers to any data link-layer network (point-to-point, broadcast)

## Slide 4: Need for address translation
Note:
  The Internet protocols are based on IP addresses
  Many link-layer networks use MAC addresses
A translation is required between IP and MAC layer addresses
  → “Given an IP address, what is the MAC address?”
IPv4 and IPv6 use different protocols for the translation:
  IPv4: Address Resolution Protocol (ARP)
  IPv6: Neighbor Discovery Protocol (NDP)

## Slide 5: Address Resolution Protocol (ARP)

## Slide 6: Overview

## Slide 7: Processing of IP packets by network device drivers
No

## Slide 8: Address translation with ARP
ARP Request: Argon broadcasts an ARP request to all stations on the network: “What is the MAC address of 128.143.137.1?”

## Slide 9: Address translation with ARP
ARP Reply: Router 137 responds with an ARP Reply which contains the MAC address
An ARP Reply is sent as a unicast Ethernet message

## Slide 10: ARP packet format

## Slide 11: Example
ARP Request from Argon:
Sender hardware address: 00:a0:24:71:e4:44 Sender protocol address: 128.143.137.144 Target hardware address: 00:00:00:00:00:00 Target protocol address: 128.143.137.1
ARP Reply from Router137:
Sender hardware address: 00:e0:f9:23:a8:20 Sender protocol address: 128.143.137.1 Target hardware address: 00:a0:24:71:e4:44 Target protocol address: 128.143.137.144

## Slide 12: ARP cache / neighbor cache
Since sending an ARP request/reply for each IP datagram is inefficient, hosts maintain a cache (ARP Cache) of current entries.
Contents of the ARP Cache: (128.143.71.37) at 00:10:4B:C5:D1:15 [ether] on eth0
  (128.143.71.36) at 00:B0:D0:E1:17:D5 [ether] on eth0
  (128.143.71.35) at 00:B0:D0:DE:70:E6 [ether] on eth0
  (128.143.136.90) at 00:05:3C:06:27:35 [ether] on eth1
  (128.143.71.34) at 00:B0:D0:E1:17:DB [ether] on eth0
Entries in the ARP cache have an expiration time:
  Entries that are not updated before their expiration time are removed
ARP cache is updated when an ARP message is received
We will also use the term neighbor cache to refer to an ARP cache

## Slide 13: Proxy ARP
Proxy ARP: Router responds to ARP Requests that arrive from one of its connected networks for a host that is on another of its connected networks

## Slide 14: Things to know about ARP
ARP Request to a non-existing host
  Several ARP requests are made with increasing time intervals between requests. Eventually, ARP gives up
Refreshing ARP cache
  On some systems, hosts periodically send ARP Requests for all addresses listed in the neighbor cache. This refreshes the neighbor cache, but also introduces traffic
Unicast ARP Requests
  Some systems send ARP Requests as unicast whenever possible
Gratuitous ARP:
  A host sends an ARP Reply with its own IP address and MAC address as a broadcast.
  Can be used to update remote neighbor caches when when a host has changed its IP address
ARP Probing
  An ARP request for ones own IP address
  Useful for detecting if an IP address has already been assigned

## Slide 15: Vulnerabilities of ARP
Since ARP does not authenticate requests or replies, ARP Requests and Replies can be forged
ARP is stateless: ARP Replies can be sent without a corresponding ARP Request
According to the ARP protocol specification, a node receiving an ARP packet (Request or Reply) must update its local ARP cache with the information in the sender field, as long as the receiving node already has an entry for the IP address of the source in its neighbor cache
Typical exploitation of these vulnerabilities:
A forged ARP Request or Reply can be used to update the neighbor cache of a remote system with a forged entry (ARP Poisoning)
This can be used to redirect IP traffic to other hosts

## Slide 16: Neighbor Discovery Part 2
ECE 461 Professor Jorg Liebeherr

## Slide 17: Neighbor Discovery Protocol (NDP)

## Slide 18: Neighbor Discovery Protocol
Uses several ICMPv6 messages types:
    Neighbor Solicitation / Neighbor Advertisement
    Router Solicitation / Router Advertisement,
    Route Redirect
Functions:
  Address resolution
  Duplicate Address Detection (DAD)
  Router/prefix/parameter discovery
  Address autoconfiguration
  Next-hop determination
  Neighbor unreachable detection
Notes: RFC 2461, Dec 1998

## Slide 19: Neighbor Discovery Protocol (NDP)
In IPv6, the Neighbor Discovery Protocol (NDP) replaces ARP
  No broadcast: NDP messages are sent as multicast or unicast
  No separate protocol: NDP messages are sent as ICMP messages
  Enhanced functions: Detection of duplicate addresses
Each node has a neighbor cache that stores (IPv6, MAC) address mappings
Two messages
  ICMP Neighbor Solicitation
  ICMP Neighbor Advertisement

## Slide 20: Node Solicitation packet format
Target address is the IPv6 address to be resolved
Option is used unless source IPv6 address is “::” It contains the MAC address of the sender of the solicitation. The address is used for the reply to the solicitation

## Slide 21: Node Advertisement packet format
Target address is the IPv6 address to be resolved
Bit flags: R (Router flag): set if sender is a router S (Solicited flag): set if this is a reply to a solicitation O (Override flag): set if this advertise-ment should override neighbor cache entry
Option is required It contains the MAC source address of the sender of the advertisement

## Slide 22: ICMP Neighbor Solicitation ICMP Neighbor Advertisement
Function:
Replacement for ARP
Duplicate Address Detection
Messages are sent via
  unicast, or
  solicited node multicast

## Slide 23: Solicited node multicast address
Suppose H1 looks for the MAC address of H3
Problem: How can H1 reach H3 without broadcast?

## Slide 24: Solicited node multicast address
Solicited node multicast address: Derive an IPv6 multicast address from unicast IPv6 address
  Fixed prefix: FF02::1:FF00:0/104
  Last 3 bytes are the last 3 bytes from unicast address and copy
1B00:0408:135D:FD0B:0D4B:2607:F2
C0:92C7
13 bytes
3 bytes
FF02:0000:0000:0000:0000:0001:FF
C0:92C7
unicast IPv6 address
solicited IPv6 multicast address

## Slide 25: Solicited node multicast address
Suppose H1 looks for the MAC address of H3
Problem: How can H1 reach H3 without broadcast?
When H3 configures its IPv6 unicast address, it starts listening to messages sent to its solicited multicast address
When H1 looks for the MAC address of H3, it sends a Neighbor Solicitation to the solicited multicast address derived from H3’s IPv6 address

## Slide 26: NDP example
Example:
Scenario: PC1 issues a ping to PC2
Observe: NDP resolves configured and link-local addresses
PC1
PC2
2606::PC1 (2606::PC2) Configured IPv6 address of PC1 (PC2) FE80::PC1 (FE80::PC2) Link-local IPv6 address of PC1 (PC2) FF02:PC2 Solicited node multicast address of PC2
PC1
PC2
2606::PC1
2606::PC2

## Slide 27: NDP Example
PC1
PC2
2606::PC1 (2606::PC2) : Configured IPv6 address of PC1 (PC2) FE80::PC1 (FE80::PC2) : Link-local IPv6 address of PC1 (PC2) FF02:PC2: Solicited node multicast address for address of PC2.
Source IPv6
Destination IPv6
Neighbor Solicitation for 2606::PC2
2606::PC1
FF02::PC2
2606::PC2
2606::PC1
Neighbor Advertisement for 2606::PC2
FE80::PC2
2606::PC1
Neighbor Solicitation for 2606::PC1
2606::PC1
FE80::PC2
Neighbor Advertisement for 2606::PC1
Neighbor Solicitation for FE80::PC2
FE80::PC1
FE80::PC2
FE80::PC2
FE80::PC1
Neighbor Advertisement for FE80::PC2
FE80::PC2
FE80::PC1
Neighbor Solicitation for FE80::PC1
FE80::PC1
FE80::PC2
Neighbor Advertisement for FE80::PC1
ICMP messages are omitted

## Slide 28: Duplicate Address Detection (DAD)
Used to determine uniqueness of an IPv6 address on a link
When a network address is configured at H1:
  H1 starts listening to the solicited node multicast address (derived from H1’s configured address)
  H1 sends an ICMP Neighbor Solicitation with its own address as target (with source address :: and the destination set to H1’s solicited node multicast address)
    If there is no response, the configured address is considered unique
    If there is a response, a duplicate address has been detected. H1 marks the address as unavailable and stops listening to the solicited node multicast address.

## Slide 29: Address Resolution for Multicast

## Slide 30: Address Translation
Unicast
128.100.11.60
00:a0:24:71:e4:44
ARP or NDP
Local broadcast
255.255.255.255
ff:ff:ff:ff:ff:ff
IPv4 only
Multicast
224.1.2.3
?
IPv4/IPv6

## Slide 31: IP Multicast
Recall: A message with a multicast destination address is sent to all receivers that have declared interest in receiving data sent to this address
Sender of 224.1.2.3
Interest in 224.1.2.3
No interest
No interest
Interest
No interest
224.1.2.3
224.1.2.3
224.1.2.3
Ethernet

## Slide 32: Approach 1: Address resolution by ARP
Send an ARP message using the MAC broadcast address ff:ff:ff:ff:ff:ff
Problem: Multiple hosts send their IP unicast address. This is not useful
Who is interested in 224.1.2.3?
Sender of 224.1.2.3
Interest in 224.1.2.3
No interest
No interest
Interest
No interest
Who is interested in 224.1.2.3?
Who is interested in 224.1.2.3?
Ethernet
Who is interested in 224.1.2.3?
Who is interested in 224.1.2.3?
Who is interested in 224.1.2.3?
I am interested! My MAC is a0:27
I am interested! My MAC is fe:3c

## Slide 33: Approach 2: Use MAC broadcast
Send every IP multicast message with destination address ff:ff:ff:ff:ff:ff in MAC header
  Messages are effectively broadcast
  Messages are filtered at non-receivers
Problem: Filtering happens in IP layer  processing overhead
Sender of 224.1.2.3
Interest in 224.1.2.3
No interest
No interest
Interest
No interest
224.1.2.3
224.1.2.3
224.1.2.3
224.1.2.3
224.1.2.3
224.1.2.3

## Slide 34: Multicast MAC address
A multicast MAC address is identified by setting the 8th bit of the first byte to “1”
A priori, a multicast Ethernet message at an Ethernet switch is sent out on all ports of the switch
    This is similar to broadcast
    Ethernet switches can mitigate the broadcast
Interfaces drop a multicast message if the receiving node is not interested in the message
    Dropping occurs at the NIC (in hardware)

## Slide 35: Multicast address mapping (IPv4)
IPv4 multicast address is statically mapped to a multicast MAC address
Last 23 bit of IP address are copied to the MAC address with fixed initial 25 bits

## Slide 36: Multicast address mapping (IPv6)
Also a static mapping
Initial 2 bytes of the MAC address are 0x3333. Remaining four bytes are copied from last four bytes of IPv6 address