## Slide 1: IP Protocol IPv4
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
You should get an idea what kind of information is kept in the IP header
The details of the fields are less important

## Slide 3: Orientation
There are currently two version in use: IPv4 (version 4) and IPv6 (Version 6)

## Slide 4: IP: The waist of the hourglass
IP has been called “the waist of the hourglass of the Internet protocol architecture”
Multiple higher-layer protocols
Multiple lower-layer protocols
Only one protocol (either IPv4 or IPv6) at the network layer

## Slide 5: Role of the IP protocol
IP is the highest layer protocol which is implemented at both routers and hosts
IP is responsible for the delivery of IP datagrams from the source to the destination(s) across a path of IP routers
IP is the only protocol that sees a multi-hop path

## Slide 6: IP service
The delivery service of IP is minimal:
  Unreliable: no attempt is made to recover lost packets
  Connectionless: each packet is handled independently
  Best effort: no guarantees are made on the service
This service is also called a datagram service
Consequences:
  Higher layer protocols have to deal with losses
  Packets may be delivered out-of-sequence

## Slide 7: IPv4 Header Format

## Slide 8: Delivery methods and IPv4 address types
Unicast ✓
Broadcast ✓
Multicast ✓
Anycast ✕
unicast
broadcast
multicast
anycast
Class A, B, C addresses
Broadcast addresses (e.g.,255.255.255.255, 128.100.255.255)
Class D addresses
There are no anycast addresses in IPv4

## Slide 9: IPv4 header format
20 bytes ≤ Header Size ≤ (24 -1) x 4 bytes = 60 bytes
20 bytes ≤ Total Length ≤ 216 -1 bytes = 65,535 bytes

## Slide 10: IPv4 header format
Version: set to 4 in IPv4
Header length: length of IP header, in multiples of 4 bytes  max. header size is (24 -1) x 4 bytes = 60 bytes

## Slide 11: IPv4 header format
Differentiated Services (DS) field
  Specifies the service and the importance desired by this datagram

## Slide 12: Differentiated services field
Specifies the service and the importance desired by this datagram
Until 1998, this field was called Type-of-Service (TOS) in IPv4
  Differentiated Service Code Point (DSCP) (6 bits)
    Used to indicate precedence (3 bits) and service level (3bits) of traffic
  Explicit Congestion Notification (ECN) (2 bits):
    Feedback mechanism used by TCP
Default behavior of routers is to ignore DSCP field
DSCP is building block to distinguish different types of traffic

## Slide 13: IPv4 header format
Total length: size of payload and header in bytes
  16 bits  216 -1 bytes = 65535 bytes is max. size

## Slide 14: IPv4 header format
The following fields play a role in IP fragmentation
Identification
Flags (3 bits): First bit always set to 0, DF bit (Do not fragment), MF bit (More fragments)
Fragment offset

## Slide 15: IPv4 header format
Time To Live (TTL)
  Specifies longest paths before datagram is dropped
  Role of TTL field: Ensure that packet is eventually dropped when a routing loop occurs
  Used as follows:
  Source sets the initial value (e.g., 64)
  Each router decrements the value by 1
  When the value reaches 0, the datagram is dropped

## Slide 16: IPv4 header format
Protocol:
    Specifies the higher-layer protocol
    Used for demultiplexing to higher layers

## Slide 17: IPv4 header format
Header checksum: A simple 16-bit long checksum which is computed for the header of the datagram

## Slide 18: IPv4 header format
Options: many options are defined, rarely used
    Record Route: each router that processes the packet adds its IP address to the header
    Timestamp: each router that processes the packet adds its IP address and time to the header
    (loose) Source Routing: specifies a list of routers that must be traversed. Replaces the destination in the IP header with the address of a router in the list.
    (strict) Source Routing: specifies a list of the only routers that can be traversed