## Slide 1: IPv4 Fragmentation
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Understand the steps of fragmentation in IPv4

## Slide 3: Maximum transmission unit (MTU)
Maximum size of IP datagram is 65535, but the data link layer protocol generally imposes a limit that is much smaller
Example:
  Ethernet frames have a maximum payload of 1500 bytes
   IP datagrams encapsulated in Ethernet frame cannot be longer than 1500 byte
The limit on the maximum IP datagram size, imposed by the data link protocol is called maximum transmission unit (MTU)
MTUs for various data link protocols (in bytes):
Ethernet | 1500
802.3 | 1492
WiFi | 2304 (mostly set to: 1500)
Minimum required | 572

## Slide 4: IP fragmentation
What if the size of an IP datagram exceeds the MTU?
IP datagram is fragmented into smaller units
What if the route contains networks with different MTUs? Fragments of an IP datagram may get fragmented again
Fragmentation:
  IP router splits the datagram into several datagram
  Fragments are reassembled at receiver

## Slide 5: Where is fragmentation done?
Fragmentation can be done at the sender or at routers
The same datagram can be fragmented several times
Reassembly of original datagram is only done at destination hosts !!

## Slide 6: What is involved in fragmentation?
The following fields in the IP header are involved:
Identification unique identification of a datagram from a host.
      Incremented whenever a datagram is transmitted.
      When a datagram is fragmented, the identification is the same in all fragments
Flags
DF bit (Do not fragment): If set, datagram cannot be fragmented and must be discarded if MTU is too small
MF bit (More fragments): If set, this datagram is a fragment and at least one additional fragment follows this one

## Slide 7: What is involved in fragmentation?
Fragment offset 1/8th of the offset of the payload of the current fragment in the original
datagram
          The fragment offset has only 13 bits
          The total length has 16 bits
             The actual offset in bytes is the value of the offset field multiplied by 8
Total length Total length of the current datagram

## Slide 8: Example of fragmentation
A datagram with size 2400 bytes must be fragmented according to an MTU limit of 1000 bytes

## Slide 9: Determining the length of fragments
Recall that, since there are only 13 bits available for the fragment offset, the offset is given as a multiple of eight bytes. As a result, the first and second fragment have a size of 996 bytes (and not 1000 bytes). This number is chosen since 976 is the largest number smaller than 1000–20= 980 that is divisible by eight. The payload for the first and second fragments is 976 bytes long, with bytes 0 through 975 of the original IP payload in the first fragment, and bytes 976 through 1951 in the second fragment. The payload of the third fragment has the remaining 428 bytes, from byte 1952 through 2379. With these considerations, we can determine the values of the fragment offset, which are 0, 976 / 8 = 122, and 1952 / 8 = 244, respectively, for the first, second and third fragment.

## Slide 10: Drawback of IP Fragmentation
Fragmentation incurs processing overhead at intermediate routers
  Performance penalty can be a factor of 10-1000
Some devices (e.g., firewalls) inspect headers of the transport protocol (e.g., port numbers)
  With fragmentation, only the first fragment of the original datagram has this header
Receiver has to reassemble the packets
  IP module at receiver must store fragments until original datagram is reconstructed
  This incurs processing overhead
  If some fragments are dropped in the network, receiver cannot reconstruct the original datagram