## Slide 1: IP Protocol IPv6
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Simplification of the IPv6 header compared to IPv4
Understand the daisy-chaining of headers using the Next header field

## Slide 3: Service of IPv6
IPv6 offers the same unreliable, connectionless, best effort service as IPv4

## Slide 4: IPv6 packet header
IPv6 has a simplified header structure:
  Headers have fixed size
  No fragmentation (available as option)
  No header checksum
Most fields play a similar role as in IPv4:
Flow label: Can be used by a source to label packets from the same flow
IPv6 | … similar to … | IPv4
Version |  | Version
Traffic class |  | DS
Payload length |  | Total length
Next Header |  | Protocol
Hop Limit |  | TTL

## Slide 5: Extension Headers
Instead of header options, IPv6 allows to concatenate optional headers to the main header
Extension Headers:
    Security: Authentication
    Fragmentation
    Routing
    Payload Header (TCP, UDP, …)

## Slide 6: IPv6 header format
Version: set to 6 in IPv6
Traffic class: same interpretation as the DS field in IPv4
Note: There is no header size field. Headers (not including header extensions) are always 40 bytes

## Slide 7: IPv6 header format
Flow label
A flow is a group of datagrams from a source to a destination (e.g., packets of a video stream)
Flow label is an identifier for a flow
Set by the source
Flow label of zero indicates that the datagram does not belong to any flow

## Slide 8: IPv6 header format
Payload length
Number of bytes following the fixed header
Max. 216 -1 bytes = 65535 bytes
Longer payloads (jumbograms) can be specified in an extension header with max. 232 -1 bytes ≈ 4 GB
Note:
Extension header is counted as payload

## Slide 9: IPv6 header format
Next Header
Two uses:
Specifies the next header:
  Routing header (43)
  Fragment header (44)
  Authentication header (51)
  Hop-by-hop option (0)
  No next header (59)
Specifies “higher layer” data:
  TCP (6)
  UDP (17)
  ICMPv6 (58)

## Slide 10: IPv6 header format
Hop limit
Same role as TTL field in IPv4
Default values (set by sources) are usually 64 or 128

## Slide 11: Fragmentation in IPv6
IPv6 allows fragmentation only at the source
  Information about offsets is stored in Fragment header
Intermediate routers never perform fragmentation
  If MTU is too small, datagram is dropped and error message (ICMP) is sent
IPv6 performs Path MTU discovery
  Path MTU = max. datagram size used between a source and a given destination
      Path MTU ≤ min. MTU on any link between source and destination
Minimum required MTU in IPv6 is 1280 bytes