## Slide 1: Internet Control Message Protocol (ICMP)
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
ICMP is a helper protocol for IP
ICMP is used for error reporting and queries
Enhanced role of ICMPv6 in IPv6:
  Neighbor discovery
  Address autoconfiguration
  Discovering multicast receivers

## Slide 3: Overview

## Slide 4: Overview
The IP (Internet Protocol) relies on several other protocols to perform necessary error reporting, support of IP configuration, routing functions
Many of these functions are provided by ICMP:
 | IPv4 | IPv6
Error signaling | ICMP | ICMPv6
Query information | ICMP | ICMPv6
Support of IP configuration | ICMP (limited) | ICMPv6
Multicast receiver discovery | IGMP | MLD (part of ICMPv6)
Setting up routing tables | RIP, OSPFv2, BGP-4 | RIPng, OSPFv3, BGP-4

## Slide 5: Overview
The Internet Control Message Protocol (ICMP) is a helper protocol that supports IP with facility for
  Error reporting
  Queries
ICMP messages are encapsulated as IP datagrams:
  In IPv4, protocol field in header is set to 1
  In IPv6, next header field in header is set to 58

## Slide 6: ICMP/ICMPv6 message format
Type: type of ICMP message
Code: subtype of ICMP message
Checksum: similar to IP header checksum. Checksum is calculated over entire ICMP message
Additional information: specific to type and code

## Slide 7: ICMP query message
ICMP query:
Request sent to a router or host
Reply sent back to querying host

## Slide 8: Example: Echo Request and Reply
Ping command issues an ICMP Echo Request
Receiver responds with an ICMP Echo Reply
Host or Router
Source
Echo Reply
ICMP
Echo Request
ICMP

## Slide 9: Format of ICMP Echo Request/Reply
Identifier, Sequence Number: Used by source to match Echo Replies with Echo Requests (Echo Reply does not modify these fields)
Payload (optional): dummy characters

## Slide 10: ICMP error message
ICMP error messages report error conditions
Typically sent when a datagram is discarded
  Error message contains parts of the discarded datagram
Error message is passed from ICMP to the application program

## Slide 11: ICMP error message
ICMP error messages includes parts of the discarded packet
  IPv4: IP header and the first 8 bytes of the payload (typically: UDP, TCP)
  IPv6: As much of the discarded packet as possible, but not exceeding minimum MTU
Information on discarded packet is used by source to pinpoint error

## Slide 12: Example: ICMP Network Unreachable
Router
If a routing table lookup does not find a match for the destination IP address, the datagram is discarded and an ICMP Network Unreachable is send to the source of the datagram
Source
No match in routing table for 10.1.0.3
IP datagram
Dst: 10.1.0.3
Network Unreachable
ICMP

## Slide 13: ICMP for IPv4

## Slide 14: ICMP Queries
Type/Code: Description
8/0 Echo Request
0/0 Echo Reply
13/0 Timestamp Request
14/0 Timestamp Reply
10/0 Router Solicitation
9/0 Router Advertisement
used by ping command
to find a router (gateway) on a subnet
for synchronization

## Slide 15: ICMP Error Message: Destination Unreachable
Type | Code | Description | 
3 | 0–15 | Destination unreachable | Notification that an IP datagram could not be forwarded and was dropped. The code field contains an explanation
Code | Description | Reason for Sending
0 | Network Unreachable | No routing table entry is available for the destination network
1 | Host Unreachable | Destination host should be directly reachable, but does not respond to ARP
2 | Protocol Unreachable | Protocol in the protocol field of the IP header not supported
3 | Port Unreachable | Transport protocol at destination cannot pass datagram to an application
4 | Fragmentation Needed and DF Bit Set | IP datagram must be fragmented, but DF bit in the IP header is set

## Slide 16: Other frequent ICMP Error message
Type | Code | Description | 
5 | 0–3 | Redirect | Informs about an alternative route for the datagram and should result in a routing table update. The code field explains the reason for the route change.
11 | 0,1 | Time exceeded | Sent when the TTL field has reached zero (Code 0) or when there is a timeout for the reassembly of IP fragments (Code 1)
12 | 0,1 | Parameter problem | Sent when the IP header is invalid (Code 0) or when an IP header option is missing (Code 1)

## Slide 17: ICMPv6

## Slide 18: ICMPv6
In IPv6, ICMP plays a bigger role
  Some IPv4-related protocols are consolidated under ICMP (ARP, IGMP)
  Combinations of ICMPv6 messages realize “subprotocols”
Neighbor Discovery Protocol (NDP)
Neighbor Solicitation/Advertisement
Router Solicitation/Advertisement Redirect Message
MTU Discovery Protocol
Packet Too Big
Multicast Listener Discovery (MLD) Protocol
Multicast Listener Query Multicast Listener Report Multicast Listener Done
Secure Neighbor Discovery (SEND) Protocol
Certification Path Solicitation Certification Path Advertisement
Multicast Router Discovery (MRD) Protocol Multicast Router Advertisement
Multicast Router Solicitation
Multicast Router Termination

## Slide 19: ICMPv6
Many queries and error messages found in ICMPv6 are similar to those in ICMP for IPv4
  Echo Request/Reply
  Destination unreachable
  …

## Slide 20: Path MTU Discovery
Recall: Intermediate IPv6 routers never perform fragmentation
Path MTU = max. datagram size used by a source to a given destination
    Path MTU ≤ min. MTU on any link between source and destination
Router issues an ICMP Packet Too Big (Type =2) if a datagram exceeds the MTU of the outgoing link
Path MTU Discovery Protocol
  Initially: Set Path MTU to the MTU at the source (on the outgoing link)
  Whenever the source receives an ICMP Packet Too Big, the source reduces the Path MTU
  This continues until no error message arrives

## Slide 21: Stateless Autoconfiguration
Refers to the automatic generation of a global unicast addresses
IPv6 address is configured without a server (stateless)
Uses ICMPv6 messages
  Router Advertisement
  Router Solicitation

## Slide 22: ICMP Router Solicitation/Advertisement
ICMP Router Solicitation is sent to the “all routers” multicast group
ICMP Router Advertisement sent to “all nodes” multicast group
Router Advertisement contains:
  Network prefix
  MTU
  Default Hop limit
  Router Advertisement may tell host to use DHCP

## Slide 23: Stateless Address Autoconfiguration
Stateless address autoconfiguration can set IP parameters of a host without a server or manual configuration:
Upon startup, host creates link-local addresses for each IPv6 interface from MAC address
Test uniqueness by sending an ICMP Neighbor Solicitation to the created address
    If a host replies with Neighbor Advertisement, address is in use
    If no response, address (and interface ID) can be used
Hosts sends ICMP Router Solicitation to “all routers” group
Router replies with ICMP Router Advertisement
Host creates a globally routable IP address using the prefix sent by the router and the Interface ID from the link-local address. Also, the advertising router becomes default gateway of host