## Slide 1: IP Forwarding
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Subnets provide a uniform logical abstractions for different types of link-layer networks
Difference between a host and a router is whether IP forwarding is enabled or not
Organization of routing tables

## Slide 3: Delivery of an IP datagram
IP
View at the data link layer layer:
  Internetwork is a collection of LANs or point-to-point links or switched networks that are connected by routers

## Slide 4: Delivery of an IP datagram
IP
View at the IP layer:
  An IP subnet is a logical entity, which we represent as a cloud
  All subnets look the same
  The IP delivery over subnets ignores the data link layer view

## Slide 5: Delivery with routing tables
destination 20.2.1.2

## Slide 6: Fundamentals for end-to-end delivery
  Having routing tables is not sufficient for end-to-end delivery
  IP and link-layer configuration must additionally satisfy a set of conditions:
Condition 1: The network prefix of a destination IP address must uniquely determine a data link layer network (The reverse need not be true!)
Condition 2: Routers and hosts with a common network prefix must be able to exchange IP datagrams using a link layer protocol
Condition 3: Data link layer networks are connected by routers to form a connected network.

## Slide 7: Processing of an IP datagram
IP router: IP forwarding enabled
Host: IP forwarding disabled

## Slide 8: Processing of an IP datagram in IP
Processing of IP datagrams is very similar on an IP router and a host
Main difference: IP forwarding is enabled on routers and disabled on hosts
IP forwarding enabled  if a datagram is received, but it is not for the local system, the datagram will be sent to a different system
IP forwarding disabled  if a datagram is received, but it is not for the local system, the datagram will be discarded

## Slide 9: Processing of an IP datagram at a router
IP header validation
Process options in IP header
Parsing the destination IP address
Routing table lookup
Decrement TTL (Hop Limit)
Perform fragmentation (if necessary)
Calculate checksum
Transmit to next hop
Send ICMP packet (if necessary)
Receive an IP datagram
IPv4 only

## Slide 10: Routing tables
Each router and host keeps a routing table which tells how to process an outgoing packet
Main columns:
    Destination (=network prefix): Where is the IP datagram going to?
    Next hop: Where to send the IP datagram to?
    Interface: What is the output interface?
Routing tables are set so that datagrams gets closer to the its destination
Destination | Next Hop | Interface
10.1.0.0/24 10.1.2.0/24 10.2.1.0/24 10.3.1.0/24 20.1.0.0/16 | on-link on-link 10.1.2.3 10.1.0.1 10.1.0.1 | eth0 serial0 serial0 eth0 eth0
Routing table of a host or router
IP datagrams is forwarded to a router (“10.1.0.1”) or directly delivered (“on-link”)
Different terms for “on-link”: directly connected, link

## Slide 11: Routing table lookup: Longest prefix match
Longest prefix match: Search for the routing table entry that has the longest match with the prefix of the destination IP address
 picks the most specific matching routing table entry
128.143.71.21
The longest prefix match for 128.143.71.21 is for 24 bits with entry 128.143.71.0/24
Datagram will be sent to R4
Destination | Next Hop
10.0.0.0/8 128.143.0.0/16 128.143.64.0/20 128.143.192.0/20 128.143.71.0/24 128.143.71.55/32 default | R1 R2 R3 R4 R4 R3

## Slide 12: Types of routing table entries
Destinations in the routing table are network prefixes
Network prefixes designate different types of routes
Network route
  Destination addresses is a network prefix (e.g., 10.0.2.0/24, 2607::2345:6789/14)
  Most entries are network routes
Host route
  Destination address is an interface address (e.g., 10.0.1.2/32, fe80::1234/128)
  Used to specify a separate route for certain hosts
Default route
  Network prefix: 0.0.0.0/0, ::/0
  The router that is listed as the next hop of the default route is the default gateway
Loopback address
  Routing table for the loopback address (127.0.0.1/32, ::1/128)
  The loopback (lo0) interface is listed as outgoing interface

## Slide 13: Routing table aggregation
Routing table entries with prefixes that form a contiguous address block and with identical next hop can be aggregated
This reduces the size of routing tables
Destination | Next Hop
10.1.0.0/24 10.1.2.0/24 10.2.1.0/24 10.3.1.0/24 20.0.0.0/14 | R3 on-link on-link R3 R2
Destination | Next Hop
10.1.0.0/24 10.1.2.0/24 10.2.1.0/24 10.3.1.0/24 20.2.0.0/15 20.0.0.0/15 | R3 on-link on-link R3 R2 R2

## Slide 14: How do routing tables get updated?
1. Configuring an IP address
  Configuring 10.0.2.3/24 on interface eth0 adds an on-link (directly connected) routing table entry
2. Adding a default gateway
  Configuring 10.0.2.1 as the default gateway adds the entry
3. Static configuration of network routes or host routes
4. Update of routing tables through routing protocols
5. ICMP messages
Destination | Next Hop | Interface
10.0.2.0/24 | on-link | eth0
Destination | Next Hop | Interface
0.0.0.0/0 | 10.0.2.1 | eth0

## Slide 15: ICMP Redirect: Routing table manipulations with ICMP
When a router detects that an IP datagram should have gone to a different router, the router (here R2)
    forwards the IP datagram to the correct router
    sends an ICMP redirect message to the host
Host uses ICMP message to update its routing table
R1