## Slide 1: Appendix to IP Forwarding: Example of Fundamental Properties
ECE 461 Professor Jorg Liebeherr

## Slide 2: Fundamentals for end-to-end delivery
  Having routing tables is not sufficient for end-to-end delivery
  IP and link-layer configuration must additionally satisfy a set of conditions:
Condition 1: The network prefix of a destination IP address must uniquely determine a data link layer network (The reverse need not be true!)
Condition 2: Routers and hosts with a common network prefix must be able to exchange IP datagrams using a link layer protocol
Condition 3: Data link layer networks are connected by routers to form a connected network.

## Slide 3: All 3 conditions are satisifed

## Slide 4: Condition 1 is not satisfied
Prefix of 10.0.11.1/24 is 10.0.1.0/24
Subnet 10.0.1.0/24 maps to 2 switches
Prefix does not uniquely determine a link-layer network
The problem:
Data link-layer network where destination 10.0.1.11 is located is ambiguous

## Slide 5: Reverse of Condition 1 is not satisfied
Switch1 supports 2 subnets: 10.0.1.0/24 and 10.0.2.0/24
2 prefixes map to the same link-layer network
No problem:
Location (at the link layer) of any destination in any of the two subnets is unique!

## Slide 6: Condition 2 not satisifed
PC1 is not connected to Switch1
Router1 and PC1 cannot exchange link-layer packets
The problem:
Destination 10.0.1.11 cannot be reached

## Slide 7: Condition 3 not satisifed
Switch3 not operational
Network consisting of data link networks connected by routers is partitioned (not connected)
The problem:
No path exists between devices connected to Switch1 and devices connected to Switch2