## Slide 1: Router Architecture
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Components of a router
Data plane vs. control plane
Architecture of a modern router

## Slide 3: Router components
Hardware components of a router:
  Network interfaces
  Interconnection network
  Processor with memory and CPU
PC router:
  Interconnection network is the (PCI) bus
  Interface cards are NICs
  All forwarding and routing is done on CPU
Commercial routers:
  Almost all forwarding is done on interface cards
  Processor is only responsible for control functions (route processor)

## Slide 4: Functional components
Control plane: routing protocols
Data plane:
per-packet processing

## Slide 5: Routing and forwarding
Two distinct aspects to delivering IP datagrams:
1. Forwarding: How to pass a packet from an input interface to the output interface?
2. Routing: How to find and setup the routing tables?
Forwarding must be done at line speed
  on routers, forwarding is supported by hardware
  on PCs, forwarding is done in kernel of the operating system
Routing is less time-critical
  routing protocols run as a background process
  routing protocols typically operate on the scale of minutes

## Slide 6: Routing and forwarding
Routing functions include:
  route calculation
  maintenance of the routing table
  execution of routing protocols
On commercial routers handled by a single general purpose processor, called route processor
IP forwarding is per-packet processing
On high-end commercial routers:
  IP forwarding is distributed
  Most work is done on interface cards

## Slide 7: Slotted chassis
Large routers have a slotted chassis
  Interface cards are inserted into slots
  Route processor is also inserted as a slot
This simplifies repairs and upgrades of components

## Slide 8: Evolution of router architectures
Early routers were essentially general purpose computers
Today, high-performance routers resemble supercomputers
    Exploit parallelism
    Special hardware components

## Slide 9: Early routers
This architecture is still used in low end routers
Arriving packets are copied to main memory via direct memory access (DMA)
Interconnection network is a backplane (shared bus)
All IP forwarding functions are performed in the central processor
Drawbacks:
  Forwarding performance is limited by CPU
  Capacity of shared bus limits the number of interface cards that can be connected

## Slide 10: “Second generation” router
Keeps shared bus architecture, but offloads most IP forwarding to interface cards
Interface cards have local route cache and processing elements
Fast path: If routing entry is found in local cache, forward packet directly to outgoing interface
Slow path: If routing table entry is not in cache, packet must be handled by central CPU
Drawback: Shared bus is still bottleneck

## Slide 11: Another “second generation” architecture
IP forwarding is done in parallel by multiple forwarding engines
Forwarding operation:
Packet received by interface: Store the packet in local memory. Extract IP header and send it to one forwarding engine
Forwarding engine does lookup, updates IP header, and sends it back to incoming interface
Packet is reconstructed and sent to outgoing interface.

## Slide 12: Modern router architecture
Interconnection network is a switch fabric, e.g., a crossbar switch
Distributed architecture:
Interface cards operate independently of each other
No centralized processing for IP forwarding
These routers can be scaled to many hundred interface cards and to an aggregate capacity of several Tbps (Terabit per second)

## Slide 13: Modern router architecture
IP Forwarding
IP Forwarding
IP Forwarding
Routing
Table
Routing
Table
Routing
Table
Switch fabric
Output
scheduling