## Slide 1: IP Address Lookup
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
CIDR enables routing table lookup that is proportional to the size of the IP address
Trie data structure for efficient lookup in a routing table
Note: With classful addresses, all entries in the routing table must be searched for a matching entries. Then, the routing lookup is proportional to the size (=number of entries) in the routing table.

## Slide 3: Modern router architecture
IP Forwarding
IP Forwarding
IP Forwarding
Routing
Table
Routing
Table
Routing
Table
Switch fabric
Output
scheduling

## Slide 4: Modern router architecture

## Slide 5: IPv4 routing table size
Source: Geoff Huston, APNIC, 2005

## Slide 6: IPv4 routing table size
Source: bgp.potaroo.net, 2013

## Slide 7: IPv4 routing table size
Source: bgp.potaroo.net, 2020

## Slide 8: IPv6 routing table size
Source: bgp.potaroo.net, 2020

## Slide 9: Routing table lookup: Longest prefix match
128.143.71.21
The longest prefix match for 128.143.71.21 is for 24 bits with entry 128.143.71.0/24
Datagram will be sent to R4
Destination | Next Hop
10.0.0.0/8 128.143.0.0/16 128.143.64.0/20 128.143.192.0/20 128.143.71.0/24 128.143.71.55/32 default | R1 R2 R3 R4 R4 R3
With CIDR, there can be multiple matches for a destination address in the routing table
Longest Prefix Match: Search for the routing table entry that has the longest match with the prefix of the destination IP address (=most specific route):
  Search for a match on all 32 bits
  Search for a match for 31 bits
  …..
  32. Search for a match on 0 bits
Needed: Data structures that support a fast longest prefix match lookup!

## Slide 10: IP address lookup algorithms
The following algorithms are suitable for longest prefix match routing table lookups
  Binary search
  Hash table
  Tries
    Binary trie
    Path-compressed trie
    Disjoint-prefix binary
    Multibit trie

## Slide 11: What is a trie?
A trie is a tree-based data structure for storing strings (dictionary):
  There is one node for each common prefix
  The strings are stored in extra leaf nodes
Tries can be used to store network prefixes
  Note: Prefixes are stored at internal nodes

## Slide 12: Binary representation of routing tables
IPv4 CIDR prefix | binary
0.0.0.0/1 | 0*
64.0.0.0/5 | 01000*
96.0.0.0/3 | 011*
128.0.0.0/1 | 1*
128.0.0.0/3 | 100*
192.0.0.0/4 | 1100*
208.0.0.0/4 | 1101*
224.0.0.0/4 | 1110*
240.0.0.0/4 | 1111*
IPv6 CIDR prefix | binary
::/1 | 0*
4000::/5 | 01000*
6000::/3 | 011*
8000::/1 | 1*
8000::/3 | 100*
C000::/4 | 1100*
D000::/4 | 1101*
E000::/4 | 1110*
F000::/4 | 1111*
IPv4 routing table
IPv6 routing table

## Slide 13: Binary trie
Search:
  Traverse the tree according to destination address
  Most recently node with a match is the current longest prefix
  Search ends when a leaf node is reached
a | 0*
b | 01000*
c | 011*
d | 1*
e | 100*
f | 1100*
g | 1101*
h | 1110*
i | 1111*
Prefixes in the table are marked (green)

## Slide 14: Binary trie (adding an entry)
Update:
  Search for the new entry
  Search ends when there is no match or a leaf node is reached
  If there is no branch to take, insert new node(s)
a | 0*
b | 01000*
c | 011*
d | 1*
e | 100*
f | 1100*
g | 1101*
h | 1110*
i | 1111*
k | 1010*
Prefixes in the table are marked (green)

## Slide 15: Compressed binary trie
Path compression
Requires to store additional information with nodes  bit number field is added to node
Bit string of prefixes must be explicitly stored at internal nodes
  Need to make comparisons when searching the tree
a | 0*
b | 01000*
c | 011*
d | 1*
e | 100*
f | 1100*
g | 1101*
h | 1110*
i | 1111*
Goal: Eliminate long sequences of 1-child nodes
Path compression  collapses 1-child branches

## Slide 16: Compressed binary trie (lookup)
Search: “010110”
Root node: Inspect 1st bit and move left
“a” node:
  Check with prefix of a (0*) and find a match
  Inspect 3rd bit and move left
“b” node:
  Check with prefix of b (01000*) and determine that there is no match
  Search stops. Longest prefix match is with a

## Slide 17: Disjoint-prefix binary trie
Nodes are split so that there is only one match for each prefix (leaf pushing)
Results:
  a (0*) is split into: a1 (00*), a3 (010*), a2 (01001*)
  d (1*) is represented as d1 (101*)
a | 0*
b | 01000*
c | 011*
d | 1*
e | 100*
f | 1100*
g | 1101*
h | 1110*
i | 1111*
Multiple matches in longest prefix rule complicate lookup
Goal: Transform tree as to avoid multiple matches

## Slide 18: Variable-stride multibit trie
2-bit stride
  1-bit prefix for a (0*) is split into 00* and 01*
  1-bit prefix for d (1*) is split into 10* and 11*
a | 0*
b | 01000*
c | 011*
d | 1*
e | 100*
f | 1100*
g | 1101*
h | 1110*
i | 1111*
Goal: Accelerate lookup by inspecting more than one bit at a time
Stride= number of bits inspected at one time
With k-bit stride, node has up to 2k child nodes

## Slide 19: Complexity of the Lookup
Complexity is expressed with O(.) (“Big–O”) notation:
  describes an asymptotic upper bound for the magnitude of a function in terms of another, usually simpler, function.
W: length of the address (32 or 128 bits)
N: number of prefixes in the routing table
k: stride
  O(n) : growth is linear with n
  O(n2): growth is quadratic with n
  O(log n): logarithmic growth in n

## Slide 20: Complexity of the lookup
Complexity is computed for
  Look-up time: What is the longest lookup time?
  Update time: How long does it take to change an entry?
  Memory: How much memory is required to store the data structure?
Scheme | Lookup | Update | Memory
Binary trie | O(W) | O(W) | O(NW)
Path-compressed trie | O(W) | O(W) | O(NW)
k-stride multibit trie | O(W/k) | O(W/k+2k) | O(2kNW/k)