## Slide 1: Routing Protocols
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Separation of control plane and data plane
Routing protocols are part of the control plane
Autonomous system
Interdomain routing vs. intradomain routing
Two approaches to shortest path routing: distance vector and link state
Acronyms: RIB, FIB, IGP, EGP
Routing protocols: RIP, OSPF, EIGRP, IS-IS, BGP

## Slide 3: Purpose of a routing protocol
Routing refers to the selection of paths (routes) between subnets, where a path is a sequence of routers
Routers maintain routing tables. An entry in the table provides the next router (next hop) on the path to a destination subnet
Routers use routing protocols to automatically set up routing tables such that the paths to destination subnets are best possible
In a routing protocol, a router exchanges information with other routers with which it shares subnets

## Slide 4: Components of a routing protocol
Exchange of reachability information between neighboring routers
Reaction to and advertising of topology changes
Calculation of optimal routes
  Usually based on a a shortest path algorithm
Terminology: Routing information exchanged between routers using a routing protocol is often called an advertisement

## Slide 5: Routing in IP

## Slide 6: Routing
There are two parts to delivering IP datagrams:
Forwarding: How to pass a packet from an input interface to the output interface of a router?
Routing: How to set up the routing tables?
Routing terminology:
  Static Routing: Routing tables are manually configured
  Dynamic Routing: Routes tables are set by routing protocols

## Slide 7: Functional components
Control plane: routing protocols
Data plane:
per-packet processing

## Slide 8: Facts about routing protocols
In principle, both hosts and routers can execute routing protocols
  Hosts rarely execute a routing protocol. If they do, they generally only listen to routing updates, but do not send updates (passive mode)
A router can simultaneously run multiple routing protocols
Each routing protocol has its own internal database

## Slide 9: RIB and FIB
Control plane: routing protocols
Data plane:
per-packet processing
Routers have separate tables for control and data plane
Routing table or Routing Information base (RIB):
  Repository where the routing protocols insert routes
  Also: directly connected networks and static routes
Forwarding table or Forwarding Information base (FIB):
  Contains same information as the routing table
  Optimized for fast lookup (e.g., trie)

## Slide 10: Administrative distance
Control plane: routing protocols
Data plane:
per-packet processing
Scenarios:
Two routing protocols compute different routes to the same destination
Static route conflicts with route computed by routing protocol
Which route to pick?
Administrative distance: Constants associated with source of routing information:
lower value  higher preference

## Slide 11: Administrative distance
Scenarios:
Two routing protocols compute different routes to the same destination
Static route conflicts with route computed by routing protocol
Which route to pick?
Administrative distance: Constants associated with source of routing information:
lower value  higher preference
Route Source | Default administrative distance
Connected interface | 0
Static route | 1
BGP (external) | 20
OSPF | 110
RIP | 120
BGP (internal) | 200
Unknown | 255

## Slide 12: Autonomous systems
An autonomous system (AS) is a region of the Internet that is administered by a single entity and that has a unified routing policy
Each autonomous system is assigned an Autonomous System Number (ASN)
Examples of autonomous systems:
    University of Toronto (ASN 239)
    Bell Canada Backbone (ASN 577)
    TekSavvy (ASN 5645)
Routing is done differently
  within an autonomous system (intradomain routing) and
  between autonomous systems (interdomain routing)

## Slide 13: Interdomain and intradomain routing
Routing protocols for intradomain routing are called interior gateway protocols (IGP)
  Objective: best (shortest) path
Routing protocols for interdomain routing are called exterior gateway protocols (EGP)
  Objective: satisfy routing policies

## Slide 14: Interdomain and intradomain routing
Intradomain Routing
Routing within an AS
Ignores the Internet outside the autonomous system
Most important routing protocols are:
  RIP
  EIGRP
  OSPF
  IS-IS
Interdomain Routing
Routing between AS’s
Assumes that the Internet consists of a collection of interconnected AS’s
Only one routing protocol:
  BGP

## Slide 15: Quagga: routing protocols on Linux systems
On Linux , routing protocols are managed through the Quagga package
Process | Routing Protocol
zebra | Routing manager (not a routing protocol)
bgpd | BGP-4
ripd | RIPv2
ospfd | OSPFv2

## Slide 16: Approaches to shortest path routing
1. Distance Vector Routing
Each router knows the distance to its directly connected neighbors
A router periodically sends a list of routing updates to its neighbors
If all routers update their distances, the routing tables eventually converge
2. Link State Routing
Each router knows the distance to its neighbors
The distance information (link state) is disseminated to all routers in the network
Each router calculates the routing tables independently

## Slide 17: Interior Gateway Protocols
Distance Vector
Routing Information protocol (RIP)
Enhanced Interior Gateway Protocol (EIGRP)
Link State
Open Shortest Path First (OSPF)
Intermediate System to Intermediate System (IS-IS)
Interior Gateway Protocol implement a shortest path algorithm