## Slide 1: Routing Information Protocol (RIP) Distance Vector Routing
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Operation of distance vector routing
Count-to-infinity problem and remedies

## Slide 3: RIP - Routing Information Protocol
A simple intradomain routing protocol
Straightforward implementation of distance vector routing
Each router advertises its distance vector every 30 seconds (or whenever its routing table changes) to its neighbors
The routing metric in RIP is the hop count
Maximum hop count is 15, with 16 interpreted as 
Routes are timeout (set to 16) after 3 minutes if they are not updated

## Slide 4: RIP - History
Late 1960s : Distance Vector protocols were used in the ARPANET
Mid-1970s: XNS (Xerox Network system) routing protocol is the precursor of RIP in IP
1982 Release of routed for BSD Unix
1988 RIPv1 (RFC 1058)
            classful routing
1993 RIPv2 (RFC 1388)
            classless routing
1997 RIPng (RFC 2080)
            support for IPv6
Current version of RIPv2 (RFC 2453)
RIP is not much used today, but it is great for studying principles of routing

## Slide 5: Notation
  Subnets are connected by routers
      subnet can be a link or a LAN
  Subnets are destinations
  Distance is measured in the number of hops to the destination subnet
      one router traversed = 1 hop
v, n, w: Routers Net(v,w): Subnet between routers v and w D(v,Net): Distance from router v to subnet Net
For simplicity, we later replace the clouds between nodes by links

## Slide 6: RIP routing table
RIP routing table stores the distance to subnets

## Slide 7: Routing messages
Routers send messages to their neighbors which contain distance information from the RIP table ( distance vector)
The distance reported in a message increments the distance from the RIP routing table by one
A message [Net , D(v,Net)+1] sent by router v to router n means: The distance from n to Net is D (v,Net)+1
v
n
[Net , D(v,Net)+1]

## Slide 8: Routing updates
Router v periodically sends the content of the RIP routing table to its neighbors

## Slide 9: Initializing RIP routing tables
Suppose a new router v becomes active
We can think about the directly connected network of having a distance of 0:
      D (v, Net(v,m)) = 0
      D (v, Net(v,w)) = 0
      D (v, Net(v,n)) = 0

## Slide 10: Initializing RIP routing tables
Then, router v advertises a distance of 1 for all directly connected networks to its neighbors

## Slide 11: Initializing RIP routing tables
Router v uses the distance vectors sent by its neighbors to build its own RIP routing table

## Slide 12: Updating RIP routing tables
Suppose router v receives the message [Net, x] from router m:
if ( x < D(v,Net) ) {
  D (v, Net) = x;
  Send message [Net, x+1] to all neighbors;
}
Router v checks if the update reduces the distance:

## Slide 13: Updating RIP routing tables
Before receiving the message:
Suppose x < D (v,Net):

## Slide 14: Example
Router A
Router B
Router C
Router D
10.0.2.0/24
10.0.3.0/24
10.0.4.0/24
10.0.5.0/24
10.0.1.0/24
.1
.2
.2
.2
.2
.1
.1
.1
Assume: - all updates occur simultaneously - Initially, each router only knows the cost of connected interfaces
t=0: 10.0.1.0 - 0 10.0.2.0 - 0
Dest. via
Dist.
t=0: 10.0.2.0 - 0 10.0.3.0 - 0
Dest. via
Dist.
t=0: 10.0.3.0 - 0 10.0.4.0 - 0
Dest. via
Dist.
t=0: 10.0.4.0 - 0 10.0.5.0 - 0
Dest. via
Dist.
t=1: 10.0.1.0 - 0 10.0.2.0 - 0 10.0.3.0 10.0.2.2 1
t=2: 10.0.1.0 - 0 10.0.2.0 - 0 10.0.3.0 10.0.2.2 1 10.0.4.0 10.0.2.2 2
t=2: 10.0.1.0 10.0.2.1 1 10.0.2.0 - 0 10.0.3.0 - 0 10.0.4.0 10.0.3.2 1 10.0.5.0 10.0.3.2 2
t=1: 10.0.1.0 10.0.2.1 1 10.0.2.0 - 0 10.0.3.0 - 0 10.0.4.0 10.0.3.2 1
t=2: 10.0.1.0 10.0.3.1 2
10.0.2.0 10.0.3.1 1 10.0.3.0 - 0 10.0.4.0 - 0 10.0.5.0 10.0.4.2 1
t=1: 10.0.2.0 10.0.3.1 1 10.0.3.0 - 0 10.0.4.0 - 0 10.0.5.0 10.0.4.2 1
t=2: 10.0.2.0 10.0.4.1 2 10.0.3.0 10.0.4.1 1 10.0.4.0 - 0 10.0.5.0 - 0
t=1: 10.0.3.0 10.0.4.1 1 10.0.4.0 - 0 10.0.5.0 - 0

## Slide 15: Example
Router A
Router B
Router C
Router D
10.0.2.0/24
10.0.3.0/24
10.0.4.0/24
10.0.5.0/24
10.0.1.0/24
.1
.2
.2
.2
.2
.1
.1
.1
t=3: 10.0.1.0 - 0 10.0.2.0 - 0 10.0.3.0 10.0.2.2 1 10.0.4.0 10.0.2.2 2 10.0.5.0 10.0.2.2 3
Dest. via
Dist.
t=3: 10.0.1.0 10.0.2.1 1 10.0.2.0 - 0 10.0.3.0 - 0 10.0.4.0 10.0.3.2 1 10.0.5.0 10.0.3.2 2
Dest. via
Dist.
t=3: 10.0.1.0 10.0.3.1 2
10.0.2.0 10.0.3.1 1 10.0.3.0 - 0 10.0.4.0 - 0 10.0.5.0 10.0.4.2 1
Dest. via
Dist.
t=3: 10.0.1.0 10.0.4.1 3 10.0.2.0 10.0.4.1 2 10.0.3.0 10.0.4.1 1 10.0.4.0 - 0 10.0.5.0 - 0
Dest. via
Dist.
Now, routing tables have converged !
t=2: 10.0.1.0 - 0 10.0.2.0 - 0 10.0.3.0 10.0.2.2 1 10.0.4.0 10.0.2.2 2
t=2: 10.0.1.0 10.0.2.1 1 10.0.2.0 - 0 10.0.3.0 - 0 10.0.4.0 10.0.3.2 1 10.0.5.0 10.0.3.2 2
t=2: 10.0.1.0 10.0.3.1 2
10.0.2.0 10.0.3.1 1 10.0.3.0 - 0 10.0.4.0 - 0 10.0.5.0 10.0.4.2 1
t=2: 10.0.2.0 10.0.4.1 2 10.0.3.0 10.0.4.1 1 10.0.4.0 - 0 10.0.5.0 - 0

## Slide 16: RIP features
Periodic Updates: Updates to the routing tables are sent every 30 seconds
Triggered Updates: If a metric changes on a link, a router immediately sends out an update without waiting for the end of the update period
Full Routing Table Update: Most distance vector routing protocol send their neighbors the entire routing table (not only entries which change)
Route invalidation timers: Routing table entries are invalid if they are not refreshed. A typical value is to invalidate an entry if no update is received after 3-6 update periods

## Slide 17: Count-to-infinity problem
A
B
Net
    Recall: In RIP,  is 16 !

## Slide 18: Count-to-infinity
The reason for the count-to-infinity problem is that each node only has a “next-hop view”
For example, in the first step, A and B do not realize that they advertise a path A-B-A-B-…
How can the count-to-infinity problem be solved?

## Slide 19: Avoiding or mitigating count-to-infinity
Path vectors: Always advertise the entire path in an update message
            In the example, B can detect if the advertised route to Net goes through B
            BGP uses this solution
Split Horizon: Never advertise the cost to a neighbor if this neighbor is the next hop on the current path
            In example: A does not send the first routing update to B, since B is the next hop on A’s current route to Net
            Split Horizon does not solve count-to-infinity in all cases!
      Triggered Updates: Whenever the metric for a route change, send an update message
            If a link goes down, neighbors are immediately notified
      Hold-down: When a route becomes unavailable, ignore routing updates about better routes for some time
            Router ignores route advertisements that seem better, but do not exist
exists in RIP

## Slide 20: RIPv2 packet format
1: request 2: response
Set to 2 for IPv4
Address of destination
Distance
2: RIPv2
Subnetmask (prefix length)
One RIP message can have up to 25 route entries
If the advertised route is not through the advertising router (otherwise set to zero)

## Slide 21: RIPv2
RIPv2 messages
  uses multicast address 224.0.0.9
  are sent in UDP messages with port number 520
Two types of messages:
  Request messages
    used to ask neighboring routers for an update
  Response messages
    contains an update

## Slide 22: Routing with RIP
Initialization: Router sends a request message on all interfaces, requesting routing tables from neighboring routers
Request received: Routers that receive a request send their entire routing table in a response message
Response received: Update the RIP routing table
Regular routing updates: Every 30 seconds, send all or part of the routing tables to every neighbor in a response message

## Slide 23: Issues with RIP
RIP takes a long time to converge
  Even for a small network, it may take several minutes until the routing tables converge after a change
Potential for count-to-infinity
The maximum path in RIP is 15 hops