## Slide 1: Open Shortest Path First (OSPF) Link State Routing
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Operation of link state routing
Components of link state routing
  Link state database
  LSA
  Reliable flooding

## Slide 3: Distance vector vs. link state routing
With distance vector routing, each node has information only about the next hop:
    Node A: to reach F go to B
    Node B: to reach F go to D
    Node D: to reach F go to E
    Node E: go directly to F
Distance vector routing makes poor routing decisions if directions are not completely correct (e.g., because a node is down).
If parts of the directions incorrect, the routing may be incorrect until the routing algorithms has re-converged.
A
B
C
D
E
F

## Slide 4: Distance vector vs. link state routing
In link state routing, each node has a complete map of the topology
If a node fails, all other nodes can calculate a new route
Difficulty: All nodes need to have a consistent view of the network
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F

## Slide 5: Link state routing: properties
Each router has complete topology information
Link state information is flooded to all nodes
Quick convergence
Link state routing are now preferred for intradomain routing

## Slide 6: Link state routing: basic principles
  Each router establishes a relationship (adjacency) with its neighbors
  Each router generates link state advertisements (LSAs) which are distributed to all routers
      Router-LSA = (router ID, list of links of router)
  Each router maintains a database of all received LSAs (link state database), which describes the network has a graph with weighted edges
  Each router uses its link state database to run a shortest path algorithm (Dijikstra’s algorithm) to compute the shortest path to each router

## Slide 7: Operation of a link state routing protocol
Received LSAs
IP Routing Table
Dijkstra’s
Algorithm
Link State Database
LSAs are flooded to other interfaces

## Slide 8: OSPF
OSPF = Open Shortest Path First
The OSPF routing protocol is the most important link state routing protocol on the Internet
The complexity of OSPF is significant
Version history:
  1989: RFC 1131 OSPF Version 1
  1991: RFC1247 OSPF Version 2
  1994: RFC 1583 OSPF Version 2 (revised)
  1997: RFC 2178 OSPF Version 2 (revised)
  1998: RFC 2328 OSPF Version 2 (current version for IPv4)
  2008: RFC 5340 OSPF Version 3 (for IPv6)

## Slide 9: Additional features of OSPF (not discussed)
Provides authentication of routing messages
Enables load balancing by allowing traffic to be split evenly across routes with equal cost
Allows hierarchical routing

## Slide 10: Example network
Router IDs are often set to one of the interface addresses, but can be set otherwise

## Slide 11: OSPF metric
Link costs are called metric
  Metric is in the range [1 , 216-1]
Metrics of a link can be asymmetric
  Metrics are set for an interface
Cost to a destination is the sum of the metrics of all traversed outgoing interfaces
Cost at R1 to R6 (10.1.7.6): 12
Cost at R6 to R1 (10.1.1.1): 15
4
4
4
5
5
5

## Slide 12: OSPF metric
To make faster links look better, the metric is often set inversely proportional to the link rate
Frequently used formula for link with rate X Mbps:
Metric)
Link rate | Metric
100 Mbps | 1
1.544 Mbps (T1) | 64
10 Mbps | 10
1 Gbps | 1

## Slide 13: Link state database
Routers exchange information about links (LSAs)
The collection of all LSAs is called the link state database
All routers have an identical link-state database
If neighboring routers discover each other for the first time, they exchange their link-state databases

## Slide 14: Network and link state database
Each router has link state database which stores the LSAs from all other routers

## Slide 15: Link state advertisement (LSA)
The Router-LSA of router 10.1.10.1 is:
Link State ID: 10.1.10.1 = Router ID
Advertising Router: 10.1.10.1 = Router ID
Number of links: 4 = 2 links + 2 subnets
Link 1: Point-to-Point, myIP = 10.1.1.1, remoteIP= 10.1.1.2, metric = 64
Link 2: Subnet, 10.1.1.0/24, , metric = 64
Link 3: Point-to-Point, myIP = 10.1.2.1, remoteIP= 10.1.2.3, metric = 64
Link 3: Subnet, 10.1.2.0/24, , metric = 64
Each router sends its Router-LSA to all routers in the network via reliable flooding

## Slide 16: Reliable flooding of LSAs
LSA-Updates are distributed to all other routers via reliable flooding
  Reliable flooding: LSA messages are acknowledged (ACK)
Example: Flooding of LSA from 10.10.10.1
LSA
LSA
Update database
Update database
ACK
ACK
LSA
LSA
LSA
LSA
ACK
ACK
ACK
Update database
Update database
ACK
ACK
ACK
ACK
ACK
Update database
ACK
LSA
LSA
ACK
ACK
LSA
LSA

## Slide 17: Dissemination of LSA
A router refloods LSAs, whenever the topology or a link cost changes
Infrequently (every 30 minutes), a router floods its LSAs even if there are no changes
Acknowledgements of LSA-updates:
    explicit ACK, or
    implicit via reception of an LSA-Update

## Slide 18: Designated Router
Routers report their links to other routers
  On a LAN, each pair of routers is a link
  Number of pairs grow quadratically with the of number of routers on a LAN:
     N routers, N(N-1)/2 pairs
OSPF avoids this, by having a designated router (DR) for each LAN
  One router becomes the DR
  DR sends a single Network-LSA for the LAN, which contains the list of all routers connected to this LAN
  Also (as before) each router sends a Router-LSA

## Slide 19: Discovery of neighbors
Routers periodically multicast OSPF Hello packets on all OSPF-enabled interfaces.
If two routers share a link, they can become neighbors and establish an adjacency
After becoming a neighbor, routers exchange their link state databases

## Slide 20: Neighbor discovery and database synchronization
Sends empty database description
Scenario: Router 10.1.10.2 restarts
Discovery of adjacency
Sends database description. (only contains LSA headers)
Database description of 10.1.10.2
Acknowledges receipt of description
After neighbors are discovered the routers exchange their link state databases

## Slide 21: Regular LSA exchanges
10.1.10.2 explicitly requests each LSA from 10.1.10.1
10.1.10.1 sends requested LSAs
10.1.10.2 has a more recent LSA (serves as implicit ACK)

## Slide 22: OSPF packet format
OSPF packets are encapsulated by IP (protocol number 89)
Destination IP address: Neighbor’s IP address or 224.0.0.5 (ALLOSPFRouters) or 224.0.0.6 (AllDRouters)
OSPF messages are generally not forwarded by routers (TTL is set to 1)

## Slide 23: OSPF packet format
2: for OSPF V2
Message types:
1: Hello (to test reachability)
2: Database description
3: Link state request
4: Link state update
5: Link state acknowledgement

## Slide 24: OSPF LSA format
LSA Header
Link 1
Link 2