## Slide 1: Spanning Tree Protocol
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Operation of the spanning tree protocol

## Slide 3: Frame forwarding
Assume a frame arrives on port x.
Is MAC address of destination in MAC table for ports A, B, or C ?
Forward the frame on the appropriate port
Flood the frame, i.e., send the frame on all ports except port x.
Found?
Not found ?

## Slide 4: Danger of loops
Consider the two LANs that are connected by two bridges.
Assume host n is transmits a frame F with unknown destination.
What will happen?
Bridges A and B flood the frame to LAN 2.
Bridge B sees F on LAN 2 (with unknown destination), and copies the frame back to LAN 1
Bridge A does the same.
The copying continues
Where is the problem? What is the solution ?
F
F
F
F
F
F
F

## Slide 5: Spanning Tree Protocol (IEEE 802.1d)
The Spanning Tree Protocol is a routing protocol to prevent loops when forwarding frames between LANs
The SPT is standardized as the IEEE 802.1d protocol
The SPT organizes bridges as a spanning tree in a dynamic environment
  Frames are forwarded only along the branches of the spanning tree
  Note: Trees don’t have loops
Bridges that run the SPT are called transparent bridges
Bridges exchange messages to configure the bridge (Configuration Bridge Protocol Data Unit or BPDUs) to build the tree.

## Slide 6: Configuration BPDUs

## Slide 7: What do the BPDUs do?
With the help of the BPDUs, bridges can:
  Elect a single bridge as the root bridge.
  Calculate the distance of the shortest path to the root bridge
  Each LAN can determine a designated bridge, which is the bridge closest to the root. The designated bridge will forward packets towards the root bridge
  Each bridge can determine its root port, which is the port that gives the best path to the root
  Select ports to be included in the spanning tree

## Slide 8: Concepts
Each bridge as a unique identifier (bridge ID)
bridge ID = priority (2 bytes) + bridge MAC address (6 bytes)
      Priority is configured
      Bridge MAC address is lowest MAC addresses of all ports
Each port of a bridge has a unique identifier (port ID)
Root bridge: Bridge with the lowest bridge ID is the root of the spanning tree
Root port: Each bridge has a root port which identifies the next hop from the bridge to the root bridge

## Slide 9: Concepts
Root path cost: For each bridge, the cost of the min-cost path to the root
Designated bridge (of a LAN): The bridge attached to a LAN that provides the min-cost path to the root for this LAN:
            If two bridges have the same cost, select the bridge with the lowest bridge ID
            Designated port: The port with which a designated bridge attaches to the LAN (for which it is the designated bridge)
            If the min-cost bridge has two or more ports on the LAN, select the port with the smaller port ID
Note: We assume that cost of a path is the number of hops

## Slide 10: Steps of Spanning Tree algorithm
Each bridge is sending out BPDUs that contain the following information:
The transmission of BPDUs results in the distributed computation of a spanning tree
root bridge (what the sending bridge thinks the root is) root path cost for sending bridge Identifies sending bridge Identifies the sending port
root ID
cost
bridge ID
port ID

## Slide 11: Ordering of messages
We define an ordering of BPDU messages
We say M1 advertises a better path to the root than M2 (“M1<<M2”) if
(R1 < R2),
Or (R1 == R2) and (C1 < C2),
Or (R1 == R2) and (C1 == C2) and (B1 < B2),
Or (R1 == R2) and (C1 == C2) and (B1 == B2) and (P1 < P2)
ID R1
C1
ID B1
M1
M2
ID P1
ID R2
C2
ID B2
ID P2

## Slide 12: Initializing the Spanning Tree Protocol
Initially, each bridge assumes that it is the root bridge
Each bridge B sends BPDUs of this form on its LANs from each port P:
A bridge compares the BPDUs received on all its ports with its own BPDU
B
0
B
P

## Slide 13: Operations of Spanning Tree Protocol
Each bridge B looks on all its ports for BPDUs that are better than its own BPDUs
Suppose that bridge B currently has BPDU:
and receives a “better” BPDU (M2<<M1):
Then B it will update the BPDU to:
The port where M2 was received becomes the root port of the bridge
R1
C1
B
--
M1
R2
C2
B2
--
M2
R2
C2+1
B
--
Note: Port numbers are set when the BDPU is transmitted

## Slide 14: When to send a BPDU?
Say, B has generated a BPDU for port x:
B sends this BPDU on port x only if the BPDU is better (via relation “<<“) than any BPDU that B received on port x.
If B sends its BPDU on port x,
  B becomes the designated bridge for the LAN to which port x connects, and
  port x becomes the designated port of that LAN
R
Cost
B
x

## Slide 15: Selecting the ports for the spanning tree
Each bridges makes a local decision which of its ports are part of the spanning tree
    The root port is part of the spanning tree
    All designated ports are part of the spanning tree
    All other ports are not part of the spanning tree
Only ports that are in the spanning tree forward frames (= forwarding state)
Ports that are not in the spanning tree do not forward frames (= blocking state)
In this way, forwarding loops are avoided

## Slide 16: Building the spanning tree
Consider the network on the right.
Assume that the bridges have calculated the designated ports (D) and the root ports (P) as indicated.
What is the spanning tree?
  On each LAN, connect R ports to the D port on this LAN
  At each switch, connect D ports to R port