## Slide 1: VLAN – Virtual LAN
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Purpose of VLANs: Separate connection to a LAN from the physical location of a host
VLAN tags

## Slide 3
  Broadcast traffic in LANs is sent to all devices on LAN
     becomes a problem in large LANs
Switch
Large LAN
Motivation

## Slide 4: Motivation
  Broadcast traffic in LANs is sent to all devices on LAN
     becomes a problem in large LANs
Traditional solution:
  Create smaller LANs
  Interconnect LANs by IP routers
  However, LAN membership of host is tied to local switch
Switch
Router
LAN 1
LAN 2
LAN 3

## Slide 5
  Broadcast traffic in LANs is sent to all devices on LAN
     becomes a problem in large LANs
Traditional solution:
  Interconnect LANs by IP routers
  However, LAN membership of host is tied to local switch
Better solution: Virtual Local Area Networks (VLANs)
VLANs separate broadcast domain from location of hosts
Used to partition large LANs
Interconnected by IP routers
Can run separate spanning tree in each VLAN
Motivation
VLAN switches
VLAN 1
VLAN 2
VLAN 3
Router

## Slide 6: Configuration of VLANs
Ports of a LAN switch can be assigned to different VLANs (via manual configuration)
VLAN 1: Ports 1,2, 5
VLAN 2: Ports 3, 4, 6
LAN switch completely separates traffic from different VLANs
  Single switch appears as multiple switches

## Slide 7: VLANs across multiple switches
If VLANs span multiple switches, then the traffic between the switches belongs to different VLANs
Switches need to be able to demultiplex traffic from different VLANs
 VLAN tags

## Slide 8: IEEE 802.1Q: VLAN Tagging
For VLAN traffic between LAN switches, add a tag to Ethernet frames that identifies the LAN
Tag can be transparent to endsystems (by stripping off VLAN tag)

## Slide 9: 802.1Q Tag Fields
Tag Protocol Identifier:
        Value 0x8100 identifies 802.1Q tag
User Priority:
        Can be used by sender to prioritize different types of traffic (e.g., voice, data)
        0 is lowest priority
Canonical Format Indicator:
        Used for compatibility between different types of MAC protocols
VLAN Identifier (VID):
        Specifies the VLAN (1 – 4094)
        0x000 indicates frame does not belong to a VLAN
        0xfff is reserved

## Slide 10: VLANs Tags
Normal operation:
Sender sends frame
First switch adds tag
Last switch removes tag

## Slide 11: More to know
We discussed port-based VLANs
  VLAN membership can be based on MAC address, protocol (e.g., IPv4, IPv6), subnet membership, TCP/UDP port, or other frame content
  Multiple VLANs per switch port is possible (used for servers)
Normal operation is to have only one spanning tree for all VLANs
  Additional protocols exist that support multiple trees