## Slide 1: Introduction to Congestion Control

## Slide 2: How does a network become congested?
Suppose a router is overloaded
Backlog at the router increases….
…until packets get delayed too long or are dropped
This causes retransmissions due to timeouts or loss detections
Retransmissions increase traffic …
…. so delays and losses at overloaded router increase
overflow

## Slide 3: What happens during congestion?
Knee – Point after which throughput increases very slowly, but delay increases fast
Cliff –
Point after which throughput starts to decrease to zero (congestion collapse) and delays grow to infinity
Good goal: Operate network near the “Knee”
Load
Load
Throughput
Delay
Knee
Cliff
congestion
collapse
packet
loss

## Slide 4
Congestion control as a feedback system
switch
Sources adjust traffic rate
Network switches
sense state (load) and feed state infor back to traffic sources
Source
Reduce traffic if load is high
Increase traffic if load is low
switch
Congestion control problem can be seen as a feedback system

## Slide 5
Congestion control as a feedback system
switch
Sources adjust traffic rate
Network switches
sense state (load) and feeds state back to traffic sources
Source
Issues to be addressed: 1. When to send feedback?
        2. How to send feedback?
        3. How to adjust rate?
switch

## Slide 6: How to detect congestion?
Explicit network signal
  Set bit in header of a packet when it encounters congestion
  Receiver returns feedback signal
Implicit network signal
  Acknowledgement for new data is interpreted as no congestion
  Packet loss is seen as sign of congestion
  TCP uses implicit congestion control signals
  (explicit signals exist, but are hardly used)

## Slide 7: Objectives of congestion control algorithm
Fairness:
  All sources should be treated “fairly”
Efficiency:
  Network resources should be well utilized
Convergence:
  Network should quickly converge to desired load level
  Load should not oscillate
Distributedness:
  No entity has complete knowledge
  Sources do not communicate with each other

## Slide 8: Binary congestion control
Network
Network Model:
Discrete time: t=1,2,3,… (feedback takes one time unit)
xi(t) : load from source i at time t
Network is represented as a single resource ( “bottleneck resource”).
Xgoal is desired load level at “Knee”
y(t): binary feedback at time t
  y(t)=0: No congestion (increase load)
  y(t) = 1: Congestion (decrease load)
Source 1
Source 2
Source n
x1
x2
xn

y
xi>Xgoal
Binary congestion control is widely used by TCP

## Slide 9: Adjusting the Rate
Additive increase, additive decrease
  aI>0, aD<0
Multiplicative increase, multiplicative decrease
  bI>1, 0<bD<1
Multiplicative increase, additive decrease
  bI>1, aD<0
Additive increase, multiplicative decrease (AIMD)
  aI>0, 0<bD<1

## Slide 10: Optimal Operating Point
User 1: x1
User 2: x2
Efficiency
line
Fairness
line
Optimal operating
point
Optimal operating point is at the intersection of fairness and efficiency lines

## Slide 11: Additive changes
User 1: x1
Efficiency
line
Fairness
line
(x1,x2)
Additive changes:
change move in a 45o angle
User 2: x2
(x1+aI,x2 +aI)
(x1+aD,x2+aD)
(x1,x2)

## Slide 12: Multiplicative changes
User 1: x1
(x1,x2)
Multiplicative changes:
change move along a line through the current point and the origin
User 2: x2
(bI x1, bIx2)
(x1, x2)
(bDx1, bDx2)

## Slide 13: Multiplicative Increase, Additive Decrease
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(x1+aD,x2+aD)
(bI(x1+aD), bI(x2+aD))
Does not converge to fairness
Does not converges to efficiency
Reaches equilibrium iff

## Slide 14: Additive Increase, Additive Decrease
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(x1+aD,x2+aD)
(x1+aD+aI), x2+aD+aI)
Does not converge to fairness
Does not converge to efficiency
Reaches equilibrium iff

## Slide 15: Multiplicative Increase, Multiplicative Decrease
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(bdx1,bdx2)
(bIbDx1, bIbDx2)
Does not converge to fairness
Stable
Converges to efficiency

## Slide 16: Additive Increase, Multiplicative Decrease (AIMD)
(bDx1+aI,bDx2+aI)
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(bDx1,bDx2)
Converges to fairness
Converges to efficiency
Increments smaller as fairness increases

## Slide 17: Importance of AIMD
Characteristics
  Only needs binary feedback information
  Converges to efficiency and fairness
  Empirical evidence shows very good performance
    Performance degrades if delays are very long
    “Proportional fairness” in a general network
AIMD-style congestion control used in most transport protocol
  Implementation of TCP congestion control introduced AIMD to Internet protocols
  Still basis for TCP congestion control