## Slide 1: Dynamic Host Configuration Protocol (DHCP)
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Dynamic assignment of IP addresses
Operation of the DHCP protocol
Lease of addresses

## Slide 3: Dynamic assignment of IP addresses
Dynamic assignment of IP addresses is desirable for several reasons:
  IP addresses are assigned on-demand
  Avoid manual IP configuration
  Support mobility of laptops
Three Protocols:
  RARP (until 1985, no longer used)
  BOOTP (1985-1993)
  DHCP (since 1993)
Only DHCP is widely used today

## Slide 4: Reverse Address Resolution Protocol (RARP)
  RARP is no longer used
  RARP client broadcasts a request for the IP address associated with a given MAC address
  RARP server responds with an IP address
  Only assigns IP address (not the default router and subnetmask)

## Slide 5: Bootstrap Protocol (BOOTP)
  Goal: Host can configure its IP parameters at boot time
  3 services:
      IP address assignment for client (with default router and subnetmask)
      IP address of the BOOTP server
      IP address of a server with a boot image
      File name of the boot image to be loaded and executed by the client
  BOOTP messages are sent over UDP:
    BOOTP server: UDP port 67 (server)
    BOOTP client: UDP port 68
    Use local broadcast address (255.255.255.255):
      This addresses is never forwarded by a router

## Slide 6: BOOTP interaction
BOOTP can be used for downloading memory image for diskless workstations
Assignment of IP addresses to hosts is static
(a)
(b)
(c)

## Slide 7: Dynamic Host Configuration Protocol (DHCP)
  DHCP is an extension of BOOTP
  In fact, a DHCP message consists of options that are attached to a BOOTP message
  Extensions:
    Supports temporary allocation (“leases”) of IP addresses
    DHCP client can acquire more configuration parameters
  DHCP is the preferred mechanism for dynamic assignment of IP addresses

## Slide 8: DHCP interaction (simplified)

## Slide 9: BOOTP/DHCP message format
(There are >100 different options)

## Slide 10: BOOTP/DHCP
Message type: 1 (Request), 2(Reply)
      Note: DHCP message type is sent in an option
Hardware type: 1 (for Ethernet)
Hardware address length: 6 (for Ethernet)
Hop count: set to 0 by client
DHCP flags: Client can set Broadcast Flag to request replies by IP broadcast (and Ethernet broadcast)
Transaction ID: integer (used to match reply to request)
Elapsed time: number of seconds since the client started to boot
Client IP address, Your IP address, server IP address, Gateway IP address, client hardware address, server host name, boot file name: client fills in the information that it has, leaves rest blank server tries to fill in the blank fields

## Slide 11: DHCP Message Type
DHCP message type is sent as an option of a BOOTP message
Value | Message Type
1 | DHCPDISCOVER
2 | DHCPOFFER
3 | DHCPREQUEST
4 | DHCPDECLINE
5 | DHCPACK
6 | DHCPNAK
7 | DHCPRELEASE
8 | DHCPINFORM

## Slide 12: Other options (selection)
Other DHCP information that is sent as an option:
  Subnet mask, IP forwarding on/off, broadcast address, router, domain name, host name, MTU, classless static route, …

## Slide 13: DHCP operation
DHCP DISCOVER
DHCP OFFER

## Slide 14: DHCP operation
DHCP Request / DHCP ACK
Only after receiving DHCP ACK can the DHCP client start to use the IP address
Renewing a lease with DHCP (sent when 50% of lease has expired)
  Lease is renewed with DHCP ACK
  IP address must be released with DHCP NACK

## Slide 15: DHCP operation
DHCP RELEASE
At this time, the DHCP client has released the IP address

## Slide 16: Broadcast or unicast
It is possible to use broadcast for the complete assignment process (DISCOVERY, OFFER, REQUEST, ACK), but unicast is frequently used:
  When DHCP client knows address of DHCP server, it may use unicast in all its messages
  The client can request a unicast reply from the server if it sets the broadcast flag to zero (request may be ignored)
  Server can send a unicast to a client without an assigned IP address by adding an ARP table entry, with the MAC address of the client and a selected IP address.

## Slide 17: DHCP relay agent
Problem: DHCP server and DHCP client are not on the same IP subnet
Destination address 255.255.255.255 is not forwarded by IP router
DHCP relay agent is a proxy that forwards DHCP requests to a DHCP server
DHCP relay agent is configured with IP addresses of DHCP server(s)