## Slide 1: Network Address Translation (NAT)
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Role of private networks and NAT router
Different uses of NAT

## Slide 3: Private IP addresses
  Both IPv4 and IPv6 reserve blocks of private IP addresses:
  Private IP addresses
    are not part of the public IP address space
    are not allocated through RIRs
    are not forwarded in the public Internet
    are not guaranteed to be unique
Comments:
  Private IPv6 addresses are called unique local (ULA) addresses
  Addressed in 100.64.0.0/10 are called carrier-grade, and are interpreted slightly differently than the other private address blocks
IPv4 | IPv6
10.0.0.0/8 172.16.0.0/12 192.168.0.0/16 (100.64.0.0/10) | fd00::/8

## Slide 4: Private network
  Private networks are networks that use private IP addresses
    IP addresses can be freely assigned from the private address space
    Private addresses can be re-used in different private networks
Consequences:
  Regular IP routers cannot forward packets from private networks to public Internet
  If a packet crosses between private network and public Internet, IP addresses in header must be modified
  → Network Address Translation

## Slide 5: Interconnecting private networks with the Internet
Private network 1
Private network 2
Observation:
  Both private networks use the same IP addresses

## Slide 6: Network Address Translation (NAT)
NAT is a router function where IP addresses (and possibly port numbers) of IP datagrams are replaced at the boundary of a private network
NAT enables hosts in private networks to communicate with hosts in the Internet
NAT router = IP router + NAT

## Slide 7: Basic operation of NAT
NAT router has an address translation table:
  Table contains address pairs: (private address, public address)
  Private network  Internet: replace private source IP address with a public IP address
  Internet  private network: replace public destination address with private IP address
NAT router

## Slide 8: Main uses of NAT
Static NAT: Make IP addresses independent from network service providers
Dynamic NAT: Pooling of IP addresses, load balancing of servers
IP masquerading: Sharing a single IP address between multiple hosts

## Slide 9: Static NAT
Static NAT: Statically configured one-to-one mapping of private and public addresses
Scenario: IP addresses in a corporate network are obtained from the service provider. Changing the service provider requires changing the IP addresses in the corporate network
NAT solution:
  Use private addresses in the corporate network
  NAT router has static entries in the address translation table that map each private address of a host in the corporate network to a public address
  Switching the network service provider (and obtaining new public IP addresses), only requires an update of the address translation table.
.

## Slide 10: Static NAT: Example
NAT router

## Slide 11: Dynamic NAT
Dynamic NAT: A pool of public IP addresses is dynamically assigned to internal hosts
Scenario: Corporate network has many hosts but only a small number of public IP addresses
NAT solution:
  Corporate network uses private IP addresses
  NAT router, located at the boundary between the corporate network and the public Internet, manages a pool of public IP addresses
  When a host from the corporate network sends an IP datagram to a host in the public Internet, the NAT router selects a public IP address from the address pool, and creates an entry in the address translation table

## Slide 12: Dynamic NAT: Example
NAT router

## Slide 13: Load balancing of servers
Scenario: Balance the load on a set of servers, which are accessible via a single IP address
NAT solution:
  Servers are assigned private addresses
  NAT router acts as a proxy for requests to the server from the public network
  NAT router changes the destination IP address of arriving packets to the private address of one of the servers
  Example of load balancing: Assign addresses of servers in a round-robin fashion

## Slide 14: Load balancing of servers
NAT router

## Slide 15: IP masquerading
Also called:
  Network address and port translation (NAPT)
  Port address translation (PAT)
  NAT overload
Scenario: A single public IP address is mapped to multiple hosts in a private network
NAT solution:
  Assign private addresses to hosts in private network
  NAT address translation table considers the port numbers
  NAT router changes both IP addresses and port numbers

## Slide 16: IP masquerading: Example
NAT router
Source port

## Slide 17: Concerns about NAT
Performance:
  Modifying the IPv4 header (changing the IP address) requires that NAT routers recalculate the IP header checksum
  Modifying port number requires that NAT routers recalculate TCP checksum
Fragmentation
  Suppose a packet is fragmented before it reaches the NAT router:
    Dynamic NAT: NAT router must assign the same IP address to each fragment
    IP Masquerading: Only the first fragment has a TCP/UDP header with a port number

## Slide 18: Concerns about NAT
End-to-end connectivity:
  NAT destroys universal end-to-end reachability of hosts on the Internet
  A priori, a host in the public Internet cannot initiate communication with a host in a private network
    Can be solved by fixing the port mapping in the address translation table (Port forwarding)
  Two hosts in different private networks cannot communicate with each other
    Requires a proxy server in the public network

## Slide 19: Concerns about NAT
IP address in application data:
  Applications that carry IP addresses in the payload of the application data generally do not work across a private-public network boundary
  Some NAT devices inspect the payload of widely used application layer protocols and, if an IP address is detected in the application-layer header or the application payload, translate the address according to the address translation table

## Slide 20: Configuring NAT in Linux
In Linux, NAT is configured with netfilter/iptables by adding filtering rules to the IP module

## Slide 21: Configuring NAT with iptables
First example: iptables –t nat –A POSTROUTING –s 10.0.1.2 –j SNAT --to-source 128.143.71.21
Network service provider migration:
iptables –t nat –R POSTROUTING –s 10.0.1.0/24 –j SNAT --to-source 128.195.4.0–128.195.4.254
Load balancing:
iptables -t nat -A PREROUTING -i eth1 -j DNAT --to-destination 10.0.1.2-10.0.1.4
Pooling of IP addresses: iptables –t nat –A POSTROUTING –s 10.0.1.0/24 –j SNAT --to-source 128.128.71.0–128.143.71.30
IP masquerading:
iptables –t nat –A POSTROUTING –s 10.0.1.0/24 –o eth1 –j MASQUERADE