## Slide 1: IP Multicast Part 1: Group management
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Semantics of IP multicast
IPv4 and IPv6 multicast addresses
Group management:
  IGMP (IPv4)
  MLD (IPv6)
  Add:
  IGMP snooping
  MLD
  Protocol type for IGMP (=2)
  Backup delay of hosts in IGMP (and MLD?)
  Check: multicast destination address of query
  Types of IGMP fields
  Why does IGMP Leave Group have destination 224.0.0.2

## Slide 3: Delivery methods
unicast
broadcast
multicast
anycast
IP Multicasting refers to the implementation of multicast communication with Internet protocols
Multicast is driven by receivers: Receivers indicate interest in receiving data

## Slide 4: Multicast Groups
The set of receivers for a multicast transmission is called a multicast group
  A multicast group is identified by a multicast IP address
  The multicast address is the destination address in all packets sent to the multicast group
  A user that wants to receive multicast transmissions joins the corresponding multicast group, and becomes a member of that group
After a user joins, the network builds the necessary routing paths so that the user receives the data sent to the multicast group

## Slide 5: Multicasting over a Packet Network
Without support for multicast at the network layer:
Multiple copies of the same data are transmitted on a link

## Slide 6: Multicasting over a Packet Network
With support for multicast at the network layer:
Requires a set of mechanisms:
Routers can forward the same packet on multiple interfaces (requires different routing table)
Multicast routing algorithm builds a distribution tree dynamically
On each link, the same data is transmitted once

## Slide 7: Semantics of IP Multicast
Multicast groups are identified by IP addresses
  IPv4: 224.0.0.0/4 (class D address)
  IPv6: FF00::/8
A host (more precisely: interface) joins and leave a multicast group dynamically
    No access control
An IP datagram send to a multicast group is transmitted to all members of the group
    Sender does not need to be a member of the group
Special case: Sender-specific multicast (SSM)
  Members request the receive packets only from specific source(s)
Delivery service of IP multicast service is unreliable

## Slide 8: The IP Protocol Stack
Network Interface
IP
IP Multicast
UDP
TCP
Socket Layer
Stream Sockets
Datagram Sockets
Multicast Sockets
User Layer
IP Multicasting only supports UDP as higher layer
There is no multicast TCP !

## Slide 9: IP Multicasting
There are three essential components of the IP Multicast service:
  Multicast addressing
  Group management
  Multicast routing
We already discussed IPv4 and IPv6 multicast addresses
For group management, we only discuss IGMP (for IPv4)

## Slide 10: Use of multicast addresses
Multicast addresses are dynamically allocated
  There is no registry for multicast addresses
  Multicast addresses should be selected so that different groups do not use the same address (address collision)
  There are diverse sets of rules how to allocate a multicast address
  There are many reserved addresses
A host (interface) can join multiple multicast groups
If a multicast address is no longer used, the multicast address is (implicitly) released.

## Slide 11: IGMP
The Internet Group Management Protocol (IGMP) supports IPv4 multicast.
IGMP is used by multicast routers to keep track of membership in a multicast group
IGMP operates within a subnet
  Hosts on a subnet announce to routers that they are members of a multicast group
  Routers ask hosts to send announcements about multicast group membership
Support for:
      Joining a multicast group
      Query membership
      Send membership reports
      Leaving a group (IGMPv2)

## Slide 12: IGMP Protocol
A host sends an IGMP report when it joins a multicast group (Note: multiple processes on a host can join. A report is sent only for the first process)
No report is sent when a process leaves a group
  Changed in IGMPv2
A multicast router regularly multicasts an IGMP query to all hosts
A host responds to an IGMP query with an IGMP report
Multicast router keeps a table of the multicast groups with joined hosts. A multicast router forwards a packet sent to a multicast group on a subnet, only if at least one host has joined the group
Note: Router does not keep track which hosts have joined

## Slide 13: IGMP Packet Format
IGMP messages are 8 bytes long
Type: 1 = sent by router, 2 = sent by host

## Slide 14: IGMP Protocol

## Slide 15: IGMP Protocol

## Slide 16: IGMP Leave Message (in IGMP version 2)
If a host leaves a multicast group and it was the last one to send a report, it sends an IGMP leave group message
Router follows up by a group specific query to make sure that there is indeed no other host in the group

## Slide 17: IGMPv3
IGMP version 3 adds the ability to join a multicast group only for specific source addresses
Can also exclude source addresses
This permits the implementation of source-specific multicast (SSM)

## Slide 18: Networks with multiple multicast routers
Only one router responds to IGMP queries (Querier)
  Router with smallest IP address becomes the querier on a network
One router forwards multicast packets to the network (Forwarder)