## Slide 1: IP Multicast Part 2: Multicast routing principles
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Approaches to multicast routing
  Source-based tree
  Core-based (shared) tree
Reverse path forwarding (RPF)
Structure of a multicast routing table
Flood-and-prune
Explicit join

## Slide 3: Multicast Routing Protocols
Goal: Build a tree that connects senders and all routers with members of a multicast group
More precisely: Build a spanning tree that connects the senders to a multicast group and routers that are connected to subnets where hosts have joined a multicast group

## Slide 4: Multicast routing as a graph problem
Problem: Embed a tree such that all multicast group members are connected by the tree

## Slide 5: Multicast routing as a graph problem
Problem: Embed a tree such that all multicast group members are connected by the tree
Solution 1: Shortest Path Tree or source-based tree Build a tree that minimizes the path cost from the source to each receiver
  Good tree if there is a single sender
  If there are multiple senders, need one tree per sender
  Easy to compute

## Slide 6: Multicast routing as a graph problem
Problem: Embed a tree such that all multicast group members are connected by the tree
Solution 2: Minimum-cost tree Build a tree that minimizes the total cost of the edges
  Good solution if there are multiple senders
  Very expensive to compute

## Slide 7: Multicast routing in practice
Routing Protocols implement one of two approaches:
  Source Based Tree:
    Essentially implements Solution 1.
    Builds one shortest path tree for each sender
    Tree is built from receiver to the sender  reverse shortest path / reverse path forwarding
  Core-based Tree:
    Build a single distribution tree that is shared by all senders
    Does not use Solution 2 (because it is too expensive)
    Selects one router as a “core” (also called “rendezvous point”)
    All receivers build a shortest path to the core  reverse shortest path / reverse path forwarding

## Slide 8: Multicast routing table
Routing table entries for source-based trees and for core-based trees are different
  Source-based tree: (Source, Group) or (S, G) entry
  Core-based tree: (*, G) entry
Source IP address | Multicast group | Incoming interface (RPF interface) | Outgoing interface list
S1 | G1 | I1 | I2, I3
* | G2 | I2 | I1, I3
I1
I2
I3

## Slide 9: Reverse Path Forwarding (RPF)
RPF builds a shortest path tree in a distributed fashion by taking advantage of the unicast routing tables
Main concept: Given the address of the root of the tree (e.g., the sending host), a router selects as its upstream neighbor in the tree the router which is the next-hop neighbor for forwarding unicast packets to the root
This concept leads to a reverse shortest path from any router to the sending host.
RPF Forwarding = Forward a packet only if it is receives from an RPF neighbor

## Slide 10: Multicast routing algorithms
Routing algorithms in practice implement one of two approaches:
  Source Based Tree:
    Establishes a reverse path from receivers to the source
  Core-based Tree:
    Establishes a reverse path to the core router

## Slide 11: Building a source-based tree
Set routing tables according to RPF forwarding
Flood-and-prune

## Slide 12: Building a source-based tree
Set routing tables according to RPF forwarding
Flood-and-prune
Flood= Forward packets on all non-RPF interfaces

## Slide 13: Building a source-based tree
Set routing tables according to RPF forwarding
Flood-and-prune
Flood= Forward packets on all non-RPF interfaces
Receiver drops packets not received on RPF interface

## Slide 14: Building a source-based tree
Set routing tables according to RPF forwarding
Flood-and-Prune
Prune= Send a prune message when a packet is received on a non-RPF interface or when there are no receivers downstream
Prune message disables routing table entry

## Slide 15: Pruning
Prune message temporarily disables a routing table entry
    Effect: Removes a link from the multicast tree
    No multicast messages are sent on a pruned link
    Prune message is sent in response to a multicast packet
    Question: Why is routing table only temporarily disabled?
Who sends prune messages?
    A router with no group members in its local network and no connections to other routers (sent on RPF interface)
    A router with no group members in its local network which has received a prune message on all non-RPF interfaces (sent on RPF interface)
    A router with group members which has received a packet from a non-RPF neighbor (to non-RPF neighbor)

## Slide 16: Building a source-based tree
When a receiver joins, one needs to re-activate a pruned routing table entry
Grafting
Sending a Graft message disables prune, and re-activates routing table entry.

## Slide 17: Alternative method for building a source-based tree
This only works if the receiver knows the source
Explicit-Join
Receiver sends IGMPv3 message, where it specifies the IP address of a source
First router sends Join message to RPF neighbor
Join message creates (S,G) routing table entry
Join message is passed on until it reaches router next to source
 source-specific multicast (SSM)

## Slide 18: Building a core-based tree
One router is the core
Receiver sends a Join message to RPF neighbor with respect to core
Join message creates (*, G) routing table entry

## Slide 19: Building a core-based tree
Source sends data to the core
Core forwards data according to routing table entry