## Slide 1: IP Multicast Part 3: Multicast routing protocols
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
Application of the principles of multicast routing (RPF) in routing protocols

## Slide 3: Multicast routing protocols in the Internet
Distance Vector Multicast Routing Protocol (DVMRP):
  First multicast routing protocol
  Assumes an “overlay” topology of multicast routers
  Implements flood-and-prune
Multicast Open Shortest Path First (MOSPF):
  Multicast extensions to OSPF. Each router calculates a shortest-path tree based on link state database
  Link state advertisements for multicast groups raises scalability concerns
Core Based Tree (CBT):
  First core-based tree routing protocol
Protocol Independent Multicast (PIM):
  Runs in two modes: PIM Dense Mode (PIM-DM) and PIM Sparse Mode (PIM-SM).
  PIM-DM builds source-based trees using flood-and-prune
  PIM-SM builds core-based trees as well as source-based trees with explicit joins.

## Slide 4: MBONE - original multicast deployment
MBone (Multicast Backbone) was the first IP multicast deployment in 1992
MBone consisted of multicast routers that exchange IP multicast datagrams over a unicast IP network
DVMRP was the routing protocol for the MBone

## Slide 5: Tunneling
MBone routers connect via IP tunnels
With tunneling, IP packets are encapsulated by another IP header (IP-in-IP encapsulation)

## Slide 6: PIM messages (PIM version 2)
PIM-DM messages | Type | PIM-DM | PIM-SM
Hello | 0 |  | 
Register | 1 |  | 
Register-Stop | 2 |  | 
Join/Prune | 3 |  | 
Bootstrap | 4 |  | 
Assert | 5 |  | 
Graft | 6 |  | 
Graft-Ack | 7 |  | 
Candidate-RP-Advertisement | 8 |  | 
Encapsulated in IP datagrams with protocol number 103
PIM messages can be sent as unicast or multicast packet
224.0.0.13 is reserved as the ALL-PIM-Routers group

## Slide 7: PIM-DM: PIM Dense Mode
PIM-DM implements flood-and-prune
Orange packet: Multicast packet (=Data)
Blue packet: Unicast PIM message

## Slide 8: PIM-SM: PIM Sparse Mode
Core is called rendezvous-point (RP)
Receivers know RP (statically configured or dynamically elected)
When receiver joins, a Join message is sent to RP on RPF.

## Slide 9: PIM-SM: PIM Sparse Mode
Host H3 joins: Join message is only forwarded until the first router that is part of the core-based tree

## Slide 10: PIM-SM: Data transmission
Source S1 sends multicast data packet
R1 sends each data packet to RP via unicast message. This is done by attaching each data packet to a unicast Register message
When data packet reaches RP, it is forwarded in the core-based tree to H2
Also: RP sends a Join message on reverse path to S1

## Slide 11: PIM-SM: Data transmission
When Join message reaches R1, R1 forwards packets from S1 as multicast packets (which reach RP)
In addition, R1 sends each data packet attached to a Register message to RP
 R1 sends two copies of the same data packet to RP

## Slide 12: PIM-SM: Data transmission
When RP receives multicast data packet, it sends a Register stop message to R1. This message stops the transmission of Register messages by R1

## Slide 13: PIM-SM: Data transmission
Now, multicast packets are sent:
  From S1 to RP
  From RP to H2

## Slide 14: PIM-SM: Switching to source-based tree
When data to receivers exceeds a threshold, routers switch to a source-based tree
This is done by sending an Explicit join message to source S1
  This sets up an reverse shortest path tree with root R1

## Slide 15: PIM-SM: Switching to source-based tree
When the reverse shortest path tree with root R1 is setup, packets on R1 are sent on two paths:
  R1  R5  R2  R3
  R1  R2  R3
There may be duplicate packets being sent for some time

## Slide 16: PIM-SM: Switching to source-based tree
At R2, when first packet arrives from R1 on its interface I1:
  R2 now receives data on RPF interface with respect to S1
  R2 sends a Prune message on its RPF with respect to RP
After the pruning, data is forwarded only along the shortest-path tree with root R1 (S1)

## Slide 17: PIM-SM for Source Specific Multicast
For Source Specific Multicast, PIM-SM only builds a source-based tree
Router simply send Join (S1,G) messages on their RPF interface with respect to S1
  where S1 is the source, and
  G is the multicast group
There is no need for a RP
∂
∂

## Slide 18: PIM-SM for Source Specific Multicast
For Source Specific Multicast, PIM-SM only builds a source-based tree
Router simply send Join (S1,G) messages on their RPF interface with respect to S1
  where S1 is the source, and
  G is the multicast group
There is no need for a RP