## Slide 1: September 29
Agenda:
  General Q&A
  4:15-4:30: Quiz
  4:30-5:00: Q&A on lecture material from previous week

## Slide 2: Review of Networking Concepts
ECE 461 Professor Jorg Liebeherr

## Slide 3: Takeaways
Review:
  Layered protocol suite
  Interactions between layered protocols
  Encapsulation and decapsulation

## Slide 4: Sending a packet from Argon to Neon

## Slide 5: Sending a packet from Argon to Neon
DNS: The IP address of “neon.tcpip-lab.edu” is 128.143.71.21
ARP: What is the MAC address of 128.143.137.1?
DNS: What is the IP address of “neon.tcpip-lab.edu”?
ARP: The MAC address of 128.143.137.1 is 00:e0:f9:23:a8:20
128.143.71.21 is not on my subnet.
Therefore, I need to send the packet to my
default gateway with address 128.143.137.1
frame
128.143.71.21 is on one of my local subnets.
Therefore, I can send the packet directly.
ARP: The MAC address of 128.143.137.1 is 00:20:af:03:98:28
ARP: What is the MAC address of 128.143.71.21?
frame
Notes: [‘;’

## Slide 6: Internet protocol suite
The Internet protocol suite is the protocol architecture of the Internet
The Internet protocol suite has four layers: Application, Transport, Internet, and Link Layer
A host implements all layers. Routers only have link and Internet layers
Note:
  Internet protocols do not actually specify a link layer
  They specify how to interface with existing link layers

## Slide 7: Internet protocols and OSI reference model
The Internet protocols do not define the lower layers of a complete protocol stack
Layer 7
Layer 6
Layer 5
Layer 4
Layer 3
Layer 2
Layer 1

## Slide 8: Assignment of protocols to layers

## Slide 9: Layered communications
A module of a given layer communicates with:
  1. a remote module a the same layer using a common protocol
  2. adjacent module at the local system via a service interface
Node A
Node B

## Slide 10: Layers in the example

## Slide 11: Layers in the example
Send HTTP Request to neon
Establish a connection to 128.143.71.21 at port 80
Open TCP connection to 128.143.71.21 port 80
Send a datagram (which contains a connection request) to 128.143.71.21
Send IP datagram to 128.143.71.21
Send the datagram to 128.143.137.1
Send Ethernet frame to 00:e0:f9:23:a8:20
Send Ethernet frame to 00:20:af:03:98:28
Send IP data-gram to 128.143.71.21
Send the datagram to 128.143.7.21
Frame is an IP datagram
Frame is an IP datagram
IP datagram is a TCP segment for port 80

## Slide 12: Encapsulation and decapsulation
As data is moving down the protocol stack, each protocol adds layer-specific control information

## Slide 13: Encapsulation and decapsulation in the example
Let us look in detail at the Ethernet frame between Argon and the Router, which contains the TCP connection request to Neon.
This is the frame in hexadecimal notation.
00e0 f923 a820 00a0 2471 e444 0800 4500 002c 9d08 4000 8006 8bff 808f 8990 808f 4715 065b 0050 0009 465b 0000 0000 6002 2000 598e 0000 0204 05b4

## Slide 14: Parsing the information in the frame

## Slide 15: Encapsulation and decapsulation

## Slide 16: Encapsulation and decapsulation: Ethernet header

## Slide 17: Encapsulation and decapsulation: IP header

## Slide 18: Encapsulation and decapsulation: IP header

## Slide 19: Encapsulation and decapsulation: TCP header
Option: maximum segment size

## Slide 20: Encapsulation and decapsulation: TCP header

## Slide 21: Encapsulation and decapsulation: TCP header

## Slide 22: Encapsulation and decapsulation: Application data
No Application Data
in this frame

## Slide 23: Different views of networking
Different Layers of the protocol stack have a different view of the network. This is HTTP’s and TCP’s view of the network

## Slide 24: Network view of IP

## Slide 25: Network view of Ethernet

## Slide 26: Data Link Protocols
ECE 461 Professor Jorg Liebeherr

## Slide 27: Takeaways
Types of data link networks
Format of a MAC address
Difference between an Ethernet switch and Ethernet hub
Format of Ethernet frames
Types of point-to-point links

## Slide 28: Internet protocol suite
The Internet protocol suite does not define data link and physical layers
Instead it takes advantage of existing lower layers, and defines interfaces to access them
Data link layers are specified by other bodies (e.g., IEEE 802)
In Internet terminology, any data link network is referred to as a “link”

## Slide 29: Data link layer (Layer 2)
The main tasks of the data link layer are:
    Transfer data from the network layer of one node to the network layer of another node
    Convert the raw bit stream of the physical layer into groups of bits (frames)

## Slide 30: Types of networks at the data link layer
  Broadcast networks: All stations share a single communication channel
    Most local area networks (LANs), e.g., Ethernet and WiFi, are broadcast networks
    Needs addresses, e.g., MAC addresses
  Point-to-Point networks: Pairs of hosts (or routers) are directly connected
    Wide area networks (WANs) are mostly point-to-point
    Addresses are not needed

## Slide 31: Medium Access Control (MAC)
In a broadcast network, the stations must ensure that only one station transmits at a time on the shared communication channel
Protocols to determine who can transmit at any time are called Medium Access Control (MAC) protocols
  Ethernet: CSMA/CD
  WiFi: CSMA/CA
MAC protocol is running on a NIC (network interface controller):
  NIC has a MAC address
Ethernet NIC

## Slide 32: MAC Addresses
A MAC address is an address of a NIC
  Also called “hardware address” or “physical address”
  Length of a MAC address is typically 6 bytes
MAC addresses are in hexadecimal notation, using “:” or “-” for byte separation: c8:2a:14:04:0a:81
    Set by manufacturer of NIC
    Intended to be permanent and globally unique
    Today, most hardware allows to change MAC addresses
Broadcast MAC address: ff:ff:ff:ff:ff:ff
Multicast MAC address: Last bit of first byte is set to “1”

## Slide 33: Ethernet Topology
There are many (>50) Ethernet variants
  Speed: 2 Mbps - 400 Gbps
  Frame formats: 802.3, Ethernet II (DIX)
Ethernet was originally designed as a bus topology
Since mid-1990s, nodes are connected to a hub or switch in a star configuration

## Slide 34: Ethernet Hubs vs. Ethernet Switches
Ethernet switch
Packet switch for Ethernet frames
Has routing table based on MAC addresses
Buffering of frames prevents collisions
Ethernet hub
Does not perform buffering
Collisions occur if two frames arrive at the same time
Frame that arrives on one port is sent out on all ports
Hub
Switch

## Slide 35: Two Ethernet frame formats
Two Ethernet frame formats are in use, with subtle differences:
  Ethernet II (DIX)
    An industry standard from 1982 that is based on the first implementation of CSMA/CD by Xerox.
    Most commonly used format
  802.3:
    IEEE’s version of CSMA/CD from 1985.
Difference for our purposes: Ethernet II and 802.3 use different methods to encapsulate IP datagrams

## Slide 36: Ethernet II encapsulation (RFC 894)

## Slide 37: IEEE 802.2/802.3 encapsulation (RFC 1042)

## Slide 38: Point-to-point links
Many data link connections are point-to-point serial links:
  Dial-in or DSL access connects hosts to access routers
  Long-distance links
Data link layer protocols for point-to-point links are simple:
  Main role is encapsulation of IP datagrams
  No media access control needed
  No address needed

## Slide 39: Data link protocols for point-to-point links
HDLC (High-Level Data Link)
  Widely used and influential standard (1979)
  Default protocol for serial links on Cisco routers
PPP (Point-to-Point Protocol)
  Based on a variant of HDLC
  Used for dial-in and for high-speed routers
Ethernet point-to-point
  Used for long-distance point-to-point links (up to 100 Gbps)

## Slide 40: PPP - IP encapsulation
The frame format of PPP is similar to HDLC and the 802.2 LLC frame format:
PPP assumes a duplex circuit
Note: PPP does not use addresses
Usual maximum frame size is 1500
Notes: PPP suports an asynchronous link (8 data bits/no parity) or a bit-oriented synchronous link

## Slide 41: Additional PPP functionality
In addition to encapsulation, PPP supports:
  Link configuration
  Link quality testing
  Error detection
  Option negotiation
  Address notification
  Authentication
The above functions are supported by helper protocols:
  LCP
  PAP, CHAP
  NCP

## Slide 42: Tunneling protocols
Tunnels are logical point-to-point links
  They appear to the endpoints as a point-to-point links
  The link is realized as a sequence of subnets

## Slide 43: Switched networks
Some data link technologies can be used to build complete networks, with their own addressing, routing, and forwarding mechanisms.
These networks are often called switched networks
At the IP layer, a switched network may appear as a point-to-point link or a broadcast link

## Slide 44: Switched networks
Data link layer technologies:
  Switched Ethernet
  Multiprotocol Label Switching (MPLS)
  ATM (Asynchronous Transfer Mode)
  Frame Relay
Some switched networks are intended for enterprise networks (Switched Ethernet), wide area networks (MPLS, Frame Relay), or both (ATM)

## Slide 45: Neighbor Discovery Part 1
ECE 461 Professor Jorg Liebeherr

## Slide 46: Takeaways
Roles of neighbor discovery (ND) and address resolution
Address resolution in IPv4 (ARP)
Address resolution in IPv6 (NDP)
Address resolution for multicast

## Slide 47: Neighbor discovery
Neighbor discovery refers protocol functions that determine link-layer addresses of nodes that are attached to the same link
In IP terminology, “link” refers to any data link-layer network (point-to-point, broadcast)

## Slide 48: Need for address translation
Note:
  The Internet protocols are based on IP addresses
  Many link-layer networks use MAC addresses
A translation is required between IP and MAC layer addresses
  → “Given an IP address, what is the MAC address?”
IPv4 and IPv6 use different protocols for the translation:
  IPv4: Address Resolution Protocol (ARP)
  IPv6: Neighbor Discovery Protocol (NDP)

## Slide 49: Address Resolution Protocol (ARP)

## Slide 50: Overview

## Slide 51: Processing of IP packets by network device drivers
No

## Slide 52: Address translation with ARP
ARP Request: Argon broadcasts an ARP request to all stations on the network: “What is the MAC address of 128.143.137.1?”

## Slide 53: Address translation with ARP
ARP Reply: Router 137 responds with an ARP Reply which contains the MAC address
An ARP Reply is sent as a unicast Ethernet message

## Slide 54: ARP packet format

## Slide 55: Example
ARP Request from Argon:
Sender hardware address: 00:a0:24:71:e4:44 Sender protocol address: 128.143.137.144 Target hardware address: 00:00:00:00:00:00 Target protocol address: 128.143.137.1
ARP Reply from Router137:
Sender hardware address: 00:e0:f9:23:a8:20 Sender protocol address: 128.143.137.1 Target hardware address: 00:a0:24:71:e4:44 Target protocol address: 128.143.137.144

## Slide 56: ARP cache / neighbor cache
Since sending an ARP request/reply for each IP datagram is inefficient, hosts maintain a cache (ARP Cache) of current entries.
Contents of the ARP Cache: (128.143.71.37) at 00:10:4B:C5:D1:15 [ether] on eth0
  (128.143.71.36) at 00:B0:D0:E1:17:D5 [ether] on eth0
  (128.143.71.35) at 00:B0:D0:DE:70:E6 [ether] on eth0
  (128.143.136.90) at 00:05:3C:06:27:35 [ether] on eth1
  (128.143.71.34) at 00:B0:D0:E1:17:DB [ether] on eth0
Entries in the ARP cache have an expiration time:
  Entries that are not updated before their expiration time are removed
ARP cache is updated when an ARP message is received
We will also use the term neighbor cache to refer to an ARP cache

## Slide 57: Proxy ARP
Proxy ARP: Router responds to ARP Requests that arrive from one of its connected networks for a host that is on another of its connected networks

## Slide 58: Things to know about ARP
ARP Request to a non-existing host
  Several ARP requests are made with increasing time intervals between requests. Eventually, ARP gives up
Refreshing ARP cache
  On some systems, hosts periodically send ARP Requests for all addresses listed in the neighbor cache. This refreshes the neighbor cache, but also introduces traffic
Unicast ARP Requests
  Some systems send ARP Requests as unicast whenever possible
Gratuitous ARP:
  A host sends an ARP Reply with its own IP address and MAC address as a broadcast.
  Can be used to update remote neighbor caches when when a host has changed its IP address
ARP Probing
  An ARP request for ones own IP address
  Useful for detecting if an IP address has already been assigned

## Slide 59: Vulnerabilities of ARP
Since ARP does not authenticate requests or replies, ARP Requests and Replies can be forged
ARP is stateless: ARP Replies can be sent without a corresponding ARP Request
According to the ARP protocol specification, a node receiving an ARP packet (Request or Reply) must update its local ARP cache with the information in the sender field, as long as the receiving node already has an entry for the IP address of the source in its neighbor cache
Typical exploitation of these vulnerabilities:
A forged ARP Request or Reply can be used to update the neighbor cache of a remote system with a forged entry (ARP Poisoning)
This can be used to redirect IP traffic to other hosts

## Slide 60: Neighbor Discovery Part 2
ECE 461 Professor Jorg Liebeherr

## Slide 61: Neighbor Discovery Protocol (NDP)

## Slide 62: Neighbor Discovery Protocol
Uses several ICMPv6 messages types:
    Neighbor Solicitation / Neighbor Advertisement
    Router Solicitation / Router Advertisement,
    Route Redirect
Functions:
  Address resolution
  Duplicate Address Detection (DAD)
  Router/prefix/parameter discovery
  Address autoconfiguration
  Next-hop determination
  Neighbor unreachable detection
Notes: RFC 2461, Dec 1998

## Slide 63: Neighbor Discovery Protocol (NDP)
In IPv6, the Neighbor Discovery Protocol (NDP) replaces ARP
  No broadcast: NDP messages are sent as multicast or unicast
  No separate protocol: NDP messages are sent as ICMP messages
  Enhanced functions: Detection of duplicate addresses
Each node has a neighbor cache that stores (IPv6, MAC) address mappings
Two messages
  ICMP Neighbor Solicitation
  ICMP Neighbor Advertisement

## Slide 64: Node Solicitation packet format
Target address is the IPv6 address to be resolved
Option is used unless source IPv6 address is “::” It contains the MAC address of the sender of the solicitation. The address is used for the reply to the solicitation

## Slide 65: Node Advertisement packet format
Target address is the IPv6 address to be resolved
Bit flags: R (Router flag): set if sender is a router S (Solicited flag): set if this is a reply to a solicitation O (Override flag): set if this advertise-ment should override neighbor cache entry
Option is required It contains the MAC source address of the sender of the advertisement

## Slide 66: ICMP Neighbor Solicitation ICMP Neighbor Advertisement
Function:
Replacement for ARP
Duplicate Address Detection
Messages are sent via
  unicast, or
  solicited node multicast

## Slide 67: Solicited node multicast address
Suppose H1 looks for the MAC address of H3
Problem: How can H1 reach H3 without broadcast?

## Slide 68: Solicited node multicast address
Solicited node multicast address: Derive an IPv6 multicast address from unicast IPv6 address
  Fixed prefix: FF02::1:FF00:0/104
  Last 3 bytes are the last 3 bytes from unicast address and copy
1B00:0408:135D:FD0B:0D4B:2607:F2
C0:92C7
13 bytes
3 bytes
FF02:0000:0000:0000:0000:0001:FF
C0:92C7
unicast IPv6 address
solicited IPv6 multicast address

## Slide 69: Solicited node multicast address
Suppose H1 looks for the MAC address of H3
Problem: How can H1 reach H3 without broadcast?
When H3 configures its IPv6 unicast address, it starts listening to messages sent to its solicited multicast address
When H1 looks for the MAC address of H3, it sends a Neighbor Solicitation to the solicited multicast address derived from H3’s IPv6 address

## Slide 70: NDP example
Example:
Scenario: PC1 issues a ping to PC2
Observe: NDP resolves configured and link-local addresses
2606::PC1 (2606::PC2) Configured IPv6 address of PC1 (PC2) FE80::PC1 (FE80::PC2) Link-local IPv6 address of PC1 (PC2) FF02:PC2 Solicited node multicast address of PC2
PC1
PC2
2606::PC1
2606::PC2

## Slide 71: NDP Example
PC1
PC2
2606::PC1 (2606::PC2) : Configured IPv6 address of PC1 (PC2) FE80::PC1 (FE80::PC2) : Link-local IPv6 address of PC1 (PC2) FF02:PC2: Solicited node multicast address for address of PC2.
Source IPv6
Destination IPv6
Neighbor Solicitation for 2606::PC2
2606::PC1
FF02::PC2
2606::PC2
2606::PC1
Neighbor Advertisement for 2606::PC2
FE80::PC2
2606::PC1
Neighbor Solicitation for 2606::PC1
2606::PC1
FE80::PC2
Neighbor Advertisement for 2606::PC1
Neighbor Solicitation for FE80::PC2
FE80::PC1
FE80::PC2
FE80::PC2
FE80::PC1
Neighbor Advertisement for FE80::PC2
FE80::PC2
FE80::PC1
Neighbor Solicitation for FE80::PC1
FE80::PC1
FE80::PC2
Neighbor Advertisement for FE80::PC1
ICMP messages are omitted

## Slide 72: Duplicate Address Detection (DAD)
Used to determine uniqueness of an IPv6 address on a link
When a network address is configured at H1:
  H1 starts listening to the solicited node multicast address (derived from H1’s configured address)
  H1 sends an ICMP Neighbor Solicitation with its own address as target (with source address :: and the destination set to H1’s solicited node multicast address)
    If there is no response, the configured address is considered unique
    If there is a response, a duplicate address has been detected. H1 marks the address as unavailable and stops listening to the solicited node multicast address.

## Slide 73: Address Resolution for Multicast

## Slide 74: Address Translation
Unicast
128.100.11.60
00:a0:24:71:e4:44
ARP or NDP
Local broadcast
255.255.255.255
ff:ff:ff:ff:ff:ff
IPv4 only
Multicast
224.1.2.3
?
IPv4/IPv6

## Slide 75: IP Multicast
Recall: A message with a multicast destination address is sent to all receivers that have declared interest in receiving data sent to this address
Sender of 224.1.2.3
Interest in 224.1.2.3
No interest
No interest
Interest
No interest
224.1.2.3
224.1.2.3
224.1.2.3
Ethernet

## Slide 76: Approach 1: Address resolution by ARP
Send an ARP message using the MAC broadcast address ff:ff:ff:ff:ff:ff
Problem: Multiple hosts send their IP unicast address. This is not useful
Who is interested in 224.1.2.3?
Sender of 224.1.2.3
Interest in 224.1.2.3
No interest
No interest
Interest
No interest
Who is interested in 224.1.2.3?
Who is interested in 224.1.2.3?
Ethernet
Who is interested in 224.1.2.3?
Who is interested in 224.1.2.3?
Who is interested in 224.1.2.3?
I am interested! My MAC is a0:27
I am interested! My MAC is fe:3c

## Slide 77: Approach 2: Use MAC broadcast
Send every IP multicast message with destination address ff:ff:ff:ff:ff:ff in MAC header
  Messages are effectively broadcast
  Messages are filtered at non-receivers
Problem: Filtering happens in IP layer  processing overhead
Sender of 224.1.2.3
Interest in 224.1.2.3
No interest
No interest
Interest
No interest
224.1.2.3
224.1.2.3
224.1.2.3
224.1.2.3
224.1.2.3
224.1.2.3

## Slide 78: Multicast MAC address
A multicast MAC address is identified by setting the 8th bit of the first byte to “1”
A priori, a multicast Ethernet message at an Ethernet switch is sent out on all ports of the switch
    This is similar to broadcast
    Ethernet switches can mitigate the broadcast
Interfaces drop a multicast message if the receiving node is not interested in the message
    Dropping occurs at the NIC (in hardware)

## Slide 79: Multicast address mapping (IPv4)
IPv4 multicast address is statically mapped to a multicast MAC address
Last 23 bit of IP address are copied to the MAC address with fixed initial 25 bits

## Slide 80: Multicast address mapping (IPv6)
Also a static mapping
Initial 2 bytes of the MAC address are 0x3333. Remaining four bytes are copied from last four bytes of IPv6 address