## Slide 1: IP Protocol IPv4
ECE 461 Professor Jorg Liebeherr

## Slide 2: Takeaways
You should get an idea what kind of information is kept in the IP header
The details of the fields are less important

## Slide 3: Orientation
There are currently two version in use: IPv4 (version 4) and IPv6 (Version 6)

## Slide 4: IP: The waist of the hourglass
IP has been called “the waist of the hourglass of the Internet protocol architecture”
Multiple higher-layer protocols
Multiple lower-layer protocols
Only one protocol (either IPv4 or IPv6) at the network layer

## Slide 5: Role of the IP protocol
IP is the highest layer protocol which is implemented at both routers and hosts
IP is responsible for the delivery of IP datagrams from the source to the destination(s) across a path of IP routers
IP is the only protocol that sees a multi-hop path

## Slide 6: IP service
The delivery service of IP is minimal:
  Unreliable: no attempt is made to recover lost packets
  Connectionless: each packet is handled independently
  Best effort: no guarantees are made on the service
This service is also called a datagram service
Consequences:
  Higher layer protocols have to deal with losses
  Packets may be delivered out-of-sequence

## Slide 7: IPv4 Header Format

## Slide 8: Delivery methods and IPv4 address types
Unicast ✓
Broadcast ✓
Multicast ✓
Anycast ✕
unicast
broadcast
multicast
anycast
Class A, B, C addresses
Broadcast addresses (e.g.,255.255.255.255, 128.100.255.255)
Class D addresses
There are no anycast addresses in IPv4

## Slide 9: IPv4 header format
20 bytes ≤ Header Size ≤ (24 -1) x 4 bytes = 60 bytes
20 bytes ≤ Total Length ≤ 216 -1 bytes = 65,535 bytes

## Slide 10: IPv4 header format
Version: set to 4 in IPv4
Header length: length of IP header, in multiples of 4 bytes  max. header size is (24 -1) x 4 bytes = 60 bytes

## Slide 11: IPv4 header format
Differentiated Services (DS) field
  Specifies the service and the importance desired by this datagram

## Slide 12: Differentiated services field
Specifies the service and the importance desired by this datagram
Until 1998, this field was called Type-of-Service (TOS) in IPv4
  Differentiated Service Code Point (DSCP) (6 bits)
    Used to indicate precedence (3 bits) and service level (3bits) of traffic
  Explicit Congestion Notification (ECN) (2 bits):
    Feedback mechanism used by TCP
Default behavior of routers is to ignore DSCP field
DSCP is building block to distinguish different types of traffic

## Slide 13: IPv4 header format
Total length: size of payload and header in bytes
  16 bits  216 -1 bytes = 65535 bytes is max. size

## Slide 14: IPv4 header format
The following fields play a role in IP fragmentation
Identification
Flags (3 bits): First bit always set to 0, DF bit (Do not fragment), MF bit (More fragments)
Fragment offset

## Slide 15: IPv4 header format
Time To Live (TTL)
  Specifies longest paths before datagram is dropped
  Role of TTL field: Ensure that packet is eventually dropped when a routing loop occurs
  Used as follows:
  Source sets the initial value (e.g., 64)
  Each router decrements the value by 1
  When the value reaches 0, the datagram is dropped

## Slide 16: IPv4 header format
Protocol:
    Specifies the higher-layer protocol
    Used for demultiplexing to higher layers

## Slide 17: IPv4 header format
Header checksum: A simple 16-bit long checksum which is computed for the header of the datagram

## Slide 18: IPv4 header format
Options: many options are defined, rarely used
    Record Route: each router that processes the packet adds its IP address to the header
    Timestamp: each router that processes the packet adds its IP address and time to the header
    (loose) Source Routing: specifies a list of routers that must be traversed. Replaces the destination in the IP header with the address of a router in the list.
    (strict) Source Routing: specifies a list of the only routers that can be traversed

## Slide 19: IPv4 Fragmentation
ECE 461 Professor Jorg Liebeherr

## Slide 20: Takeaways
Understand the steps of fragmentation in IPv4

## Slide 21: Maximum transmission unit (MTU)
Maximum size of IP datagram is 65535, but the data link layer protocol generally imposes a limit that is much smaller
Example:
  Ethernet frames have a maximum payload of 1500 bytes
   IP datagrams encapsulated in Ethernet frame cannot be longer than 1500 byte
The limit on the maximum IP datagram size, imposed by the data link protocol is called maximum transmission unit (MTU)
MTUs for various data link protocols (in bytes):
Ethernet | 1500
802.3 | 1492
WiFi | 2304 (mostly set to: 1500)
Minimum required | 572

## Slide 22: IP fragmentation
What if the size of an IP datagram exceeds the MTU?
IP datagram is fragmented into smaller units
What if the route contains networks with different MTUs? Fragments of an IP datagram may get fragmented again
Fragmentation:
  IP router splits the datagram into several datagram
  Fragments are reassembled at receiver

## Slide 23: Where is fragmentation done?
Fragmentation can be done at the sender or at routers
The same datagram can be fragmented several times
Reassembly of original datagram is only done at destination hosts !!

## Slide 24: What is involved in fragmentation?
The following fields in the IP header are involved:
Identification unique identification of a datagram from a host.
      Incremented whenever a datagram is transmitted.
      When a datagram is fragmented, the identification is the same in all fragments
Flags
DF bit (Do not fragment): If set, datagram cannot be fragmented and must be discarded if MTU is too small
MF bit (More fragments): If set, this datagram is a fragment and at least one additional fragment follows this one

## Slide 25: What is involved in fragmentation?
Fragment offset 1/8th of the offset of the payload of the current fragment in the original
datagram
          The fragment offset has only 13 bits
          The total length has 16 bits
             The actual offset in bytes is the value of the offset field multiplied by 8
Total length Total length of the current datagram

## Slide 26: Example of fragmentation
A datagram with size 2400 bytes must be fragmented according to an MTU limit of 1000 bytes

## Slide 27: Determining the length of fragments
Recall that, since there are only 13 bits available for the fragment offset, the offset is given as a multiple of eight bytes. As a result, the first and second fragment have a size of 996 bytes (and not 1000 bytes). This number is chosen since 976 is the largest number smaller than 1000–20= 980 that is divisible by eight. The payload for the first and second fragments is 976 bytes long, with bytes 0 through 975 of the original IP payload in the first fragment, and bytes 976 through 1951 in the second fragment. The payload of the third fragment has the remaining 428 bytes, from byte 1952 through 2379. With these considerations, we can determine the values of the fragment offset, which are 0, 976 / 8 = 122, and 1952 / 8 = 244, respectively, for the first, second and third fragment.

## Slide 28: Drawback of IP Fragmentation
Fragmentation incurs processing overhead at intermediate routers
  Performance penalty can be a factor of 10-1000
Some devices (e.g., firewalls) inspect headers of the transport protocol (e.g., port numbers)
  With fragmentation, only the first fragment of the original datagram has this header
Receiver has to reassemble the packets
  IP module at receiver must store fragments until original datagram is reconstructed
  This incurs processing overhead
  If some fragments are dropped in the network, receiver cannot reconstruct the original datagram

## Slide 29: IP Protocol IPv6
ECE 461 Professor Jorg Liebeherr

## Slide 30: Takeaways
Simplification of the IPv6 header compared to IPv4
Understand the daisy-chaining of headers using the Next header field

## Slide 31: Service of IPv6
IPv6 offers the same unreliable, connectionless, best effort service as IPv4

## Slide 32: IPv6 packet header
IPv6 has a simplified header structure:
  Headers have fixed size
  No fragmentation (available as option)
  No header checksum
Most fields play a similar role as in IPv4:
Flow label: Can be used by a source to label packets from the same flow
IPv6 | … similar to … | IPv4
Version |  | Version
Traffic class |  | DS
Payload length |  | Total length
Next Header |  | Protocol
Hop Limit |  | TTL

## Slide 33: Extension Headers
Instead of header options, IPv6 allows to concatenate optional headers to the main header
Extension Headers:
    Security: Authentication
    Fragmentation
    Routing
    Payload Header (TCP, UDP, …)

## Slide 34: IPv6 header format
Version: set to 6 in IPv6
Traffic class: same interpretation as the DS field in IPv4
Note: There is no header size field. Headers (not including header extensions) are always 40 bytes

## Slide 35: IPv6 header format
Flow label
A flow is a group of datagrams from a source to a destination (e.g., packets of a video stream)
Flow label is an identifier for a flow
Set by the source
Flow label of zero indicates that the datagram does not belong to any flow

## Slide 36: IPv6 header format
Payload length
Number of bytes following the fixed header
Max. 216 -1 bytes = 65535 bytes
Longer payloads (jumbograms) can be specified in an extension header with max. 232 -1 bytes ≈ 4 GB
Note:
Extension header is counted as payload

## Slide 37: IPv6 header format
Next Header
Two uses:
Specifies the next header:
  Routing header (43)
  Fragment header (44)
  Authentication header (51)
  Hop-by-hop option (0)
  No next header (59)
Specifies “higher layer” data:
  TCP (6)
  UDP (17)
  ICMPv6 (58)

## Slide 38: IPv6 header format
Hop limit
Same role as TTL field in IPv4
Default values (set by sources) are usually 64 or 128

## Slide 39: Fragmentation in IPv6
IPv6 allows fragmentation only at the source
  Information about offsets is stored in Fragment header
Intermediate routers never perform fragmentation
  If MTU is too small, datagram is dropped and error message (ICMP) is sent
IPv6 performs Path MTU discovery
  Path MTU = max. datagram size used between a source and a given destination
      Path MTU ≤ min. MTU on any link between source and destination
Minimum required MTU in IPv6 is 1280 bytes